## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Metrics (1.2)

## Slide 2: Dependability

## Slide 3: Dependability
Computer failure at all layers
  Software crash
  hardware faults
    CPU Failure when dense
    Power loss, network partition
Failures are common for large systems
  Large number of desktops:
  Desktop machines are prone to failure
  More likely to fail with more machines

## Slide 4: Dependability is important
The case of SLA (Service Level Agreement)
  Between cloud provider and customer
  Anticipated latency for a request.
    “99% requests completed within 100 msec.”
  When SLA violated, Amazon pays you $ back

## Slide 5: Defining failure
Service accomplishment(A): satisfying SLA
Service interruption(I): violating SLA
Failure: state A  state I
Restorations: state I  state A
A
Failure
Restorations
Time-line
I
Failure

## Slide 6: Quantitative Dependability Metrics
Module reliability
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF) = MTTF + MTTR
Module availability = MTTF / MTBF
Failure
Restorations
Time-line
MTTR
MTTF
MTBF
I
Failure
A

## Slide 7: Overall dependability
…
Disk subsystem

## Slide 8: Overall dependability
…
Disk subsystem

## Slide 9: Evaluation
Consider a computer of a CPU, a main memory, a disk device, a keyboard, a network card and a power supply module. Each component has an MTTF of 1 million hours. What is the overall MTTF of running our “hello” demo (repeated) on this computer?
Notes: 200,000 hour MTTF (because network card does not affect the demo).

## Slide 10: Measuring Perf. With Benchmarks

## Slide 11: Performance metrics
Two common metrics
  Latency (how long to do X)
    Also called response time and execution time
  Throughput (how often can it do X)
Analogy to car assembly line
  Takes 6 hours to make a car (latency is 6 hours per car)
  A car leaves every 5 minutes (throughput is 12 cars per hour)
  Overlap results in Throughput > 1/Latency
Notes: Throughput -> parallel and concurrency

## Slide 12: Benchmark: Why
Performance dependent to system setup and workload.
  Latency of Program A on CPU A is not that of Program A on CPU B.
Performance comparison
  CPU A is faster than CPU B
  Fair comparison: same programs, same memory, etc
This is benchmark!
Standardized system setup and workloads

## Slide 13: Benchmark Types
Real applications and application suites
  Desktop: SPEC CPU2006 (INT/FLOATP)
  Server:
    CPU: SPECrate,MPI, OpenMP
    IO: SPECWeb, SPECSFS, TPC suites
  Embedded system: Dhrystone, EEMBC
Kernels, top programs, synthetic benchmarks
  Kernel: “Representative” parts of real applications
  Toy/synthetic bchmrks: stress-test functions/features
  Easier and quicker to set up and run
  Often not really representative of the entire app
Notes: Synthetic is not reliable as kernel benchmark

## Slide 14: SPEC CPU (integer)
“Representative” applications keeps growing with time!

## Slide 15: SPEC CPU (floating point)

## Slide 16: TPC Benchmark Suit (DB)
Measure transaction-processing throughput
Benchmarks for different scenarios
  TPC-C: warehouses and sales transactions
  TPC-H: ad-hoc decision support
  TPC-W: web-based business transactions
  YCSB[1]: cloud serving applications
Setup:
  Requires full OS support, a working DBMS
  Long simulations to get stable results
Notes: Ycsb -> yahoo cloud serving benchmark

## Slide 17: Price-Performance
Notes: Fp > floating point computation, int -> integer computation

## Slide 18: CPU Perf. and Speedup

## Slide 19: CPU Performance Equation (1)
Hardware Technology, Organization
Organization, ISA
ISA, Compiler Technology
A.K.A. The “iron law” of performance
Notes: Cpu time = number of seconds/number of programs gives time to run each program

## Slide 20: CPU Time example
Program takes 33 billion instructions to run
CPU processes instructions at 2 cycles per inst
Clock speed of 3GHz
= 22 seconds
33*10^9/1
2/1
1/3*10^9

## Slide 21: CPU Performance Equation (2)
For each type of instruction
How many instructions of the type are there in the program
How many cycles it takes to execute an instruction of the type
Notes: Load and store instructions
ALU instructions
Jump or branch instructions
Cycles to run these instructions are different

## Slide 22: CPU performance w/ different insts
Instruction Type | Frequency | CPI
Integer | 40% | 1.0
Branch | 20% | 4.0
Load | 20% | 2.0
Store | 10% | 3.0
Total Insts = 50B, Clock speed = 2 GHz
=50*10^9*(1.0*0.4 + 4.0*0.2 + 2.0*0.2 + 3.0*0.1)*1/2/10^9 =47.5

## Slide 23: Comparing Performance: Speedup
“X is n times faster than Y”
Execution time
  Wall clock time: includes all system overheads, user-perceivable time
  CPU time: only computation time
    Exclude the IO wait time…
“Throughput of X is n times that of Y”
Notes: time loop.sh (understand user time, system time, real time)

## Slide 24: Relation to benchmark
“X is n times faster than Y on A”
Speedup might be specific to the running benchmark
  X is 10 times faster than Y on A, and 1.5 times on B, but Y is 2 times faster than X on C, and 3 times on D, and…
So does X have better performance than Y?
Which would you buy?

## Slide 25: Summarizing Performance
Arithmetic mean
  Average execution time
  Gives more weight to longer-running programs
Weighted arithmetic mean
  More important programs can be emphasized
  But what do we use as weights?
  Different weight will make different machines look better

## Slide 26: Speedup
 | Machine A | Machine B
Program 1 | 5 sec | 4 sec
Program 2 | 3 sec | 6 sec
What is the speedup of A compared to B on Program 1?
What is the speedup of A compared to B on Program 2?
What is the average speedup?
What is the speedup of A compared to B on Sum(Program1, Program2) ?
4/5
6/3
½*(4/5 + 6/3)
(4 + 6)/(5 + 3)

## Slide 27: Amdahl’s Law

## Slide 28: Amdahl’s Law (1)
What if enhancement does not enhance everything?
Notes: 1- Fraction -> part that is not affected by optimisation
Speedup -> fraction enhanced by optimisation

## Slide 29: Amdahl’s Law (2)
Make the Common Case Fast
VS
Important: Principle of locality Approx. 90% of the time spent in 10% of the code

## Slide 30: Car Analogy
Turbo – no benefit when stuck in traffic
  10 miles at 50 mph on highway (100 mph with turbo)
  2 miles at 10 mph on campus (no benefit from turbo)
  Overall speedup?
  Sol:
    10 mile highway: 12 min
    2 mile campus road: 12 min
    S = 1 / (1/2 + 1/2/2) = 1.333

## Slide 31: Price-Performance
Hey, turbo is still a net win (we get there faster)
Consider the cost, too:
  Without Turbo
    Car costs $8,000 to manufacture
    Selling price is $12,000  $4K profit per car
    If we sell 10,000 cars, that’s $40M in profit
  With Turbo
    Car costs extra $3,000
    Selling price is $16,000  $5K profit per car
    But only a few gear heads buy the car:
      We only sell 400 cars and make $2M in profit

## Slide 32: CPU Design is Similar
How much effective performance do I get out of it?
  100% speedup for small fraction of time wasn’t a big win for the car example
How much more do I have to charge for it?
  Extra development, testing, marketing costs
How much more can I charge for it?
  Does the market even care?
  How does the price change affect volume?

## Slide 33: Another Car Analogy
Let’s say we already have Turbo… now Turbo++
  Now 200 mph with Turbo++ on 10 miles of highway
  Still no benefit on campus (2 miles)
  Overall speedup of Turbo++ over Turbo? Is it the same as overall speedup of Turbo over “Plain”
  No! The “Fraction improved” part has changed!

## Slide 34: Amdahl’s Law (3)
Diminishing Returns
Green Phase
Blue Phase
Total Execution Time
Generation 1
Green
Blue
Total Execution Time
Generation 2
Generation 3
Blue
Total Execution Time
over Generation 2
over Generation 1