## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
CPU: ISA & Pipelining (2.1)

## Slide 2: ISA

## Slide 3: ISA Principles
ISA design: instruct ALU (or MUX, etc) to work
Memory
CPU internal storage:
  Stack
  Accumulator
  General register
    Register-memory
    Register-register

## Slide 4: ISA Principles: internal storage
C = A + B (A,B,C in memory)

## Slide 5: ISA Principles: Others
Type of operands:
  Granularity of memory objects:
    1 byte (8), half-word/Short(16), or word/Integer (32)
Memory addressing:
  Byte ordering in an object: big/little endian
    0x56: 56(l), 65(b)
Type of operations:
  ALU, data transfer, control, system, FP, etc
Control flow (not PC+X)
  Jumps, conditional branch, procedure calls/returns, (interrupt/exception), syscall, etc

## Slide 6: X86 (a CISC ISA)
Register-memory
Byte-addressing
  Words are stored in memory with little-endian byte order.
Memory segmentation
  DS: stack, heap, etc
  CS
  Demo: /proc/self/maps
Operating modes: real, long, protected (ring 0-3)
General-purpose registers: eax,rbx, r8-15, etc
The case of x86-64
  - 64-bit general-purpose processor registers (e.g. rax, rbx),
  - 64-bit integer arithmetic and logical operations,
  - 64-bit virtual addresses.

## Slide 7: RISC
RISC: Simplify
Internal storage: Load-store register
32 registers (MIPS), each per 32 or 64 bits.
Few instructions:
  ALU instr:
    ADD R1, R2, R3
  Load/store instr:
    LD R1, A
  Branch/jumps:
    BEQ addr.

## Slide 8: Simple RISC Implementation
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
Memory
DrMEM
DrALU
DrPC
ALU
func
WrMEM
Addr Din
Dout
Regs
DrREG
Din
Dout
regno
WrREG
IR
LdIR

## Slide 9: Pipelining (5-stage)

## Slide 10: Oil Transport Analogy
Plan A: Move 1,000,000 gallons of oil at a time
  Buy a tanker ship, then repeat:
    Fill with oil, sail for 30 days, empty, go back
Plan B: Move 100 gallons of oil at a time
  Buy a speedboat, then repeat:
    Take barrel of oil, sail for 2 days, unload, go back
Plan C: Deep pipelining

## Slide 11: RISC’s 5-stage pipeline
Instructions impl. in 5 stages
  IF(instruction fetch): fetch based on PC
  ID(instruction decode): read I and Reg.
  EX(Execution): ALU operations
  MEM (Memory access): LD/SD
  WB: Write-back cycles: result  Reg

## Slide 12: Pipelined
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
IF
WB
EX
MEM
ID
Notes: SE: sign-extend from 16-bit to 32-bit, without changing sign and values.
MX: for multiplication operations
A: address
D: data

## Slide 13: Without pipeline – done in 1 cycle
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
Control instruction
ALU/Mem instruction

## Slide 14: Without pipeline
Instruction takes 1 cycle
1 cycle (non-pipeline) : 5 usec
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
1 clock

## Slide 15: With pipeline – Cycle 1
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
IF
WB
EX
MEM
ID

## Slide 16: With pipeline – Cycle 2
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
IF
WB
EX
MEM
ID

## Slide 17: With pipeline – Cycle 3
IF
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
WB
EX
MEM
ID

## Slide 18: With pipeline – Cycle 4
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
IF
WB
EX
MEM
ID

## Slide 19: With pipeline – Cycle 5
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
ADD
ADD
ALU
1
A
D
BEQ
IF
WB
EX
MEM
ID

## Slide 20: With pipeline: Is it faster?
Instruction takes 5 cycles now!
1 cycle (pipelined) : 1 usec = 5 usec/5 stages
1 clock
Throughput improved:
“3 instr. in 7 usec” vs “3 instr. in 15 usec”

## Slide 21: What about latency?
Instruction latency longer now
  Latch at end of each stage adds latency
  Longest stage determines clock cycle time
  Example:
Pipelining is for instruction throughput, not latency!!!
IF | 1.0 ns
ID | 0.6 ns
EX | 0.9 ns
MEM | 1.2 ns
WB | 0.4 ns
Design | Cycle time | # of cycles | Inst Latency
1-stage | 4.1 ns (sum) | 1 | 4.1 ns
5-stage | 1.2 ns (max) | 5 | 6.0 ns

## Slide 22: Super-pipelining!
Speedup ~ number of stages
Idea: let’s have a lot of stages
  How about >30? Think Pentium 4.
  Clock / 30  higher clock frequency!
How about 10000 pipeline stages?!
Problem: hurdles of pipelining!
  Will be covered in next class.