## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
ILP Data-Hazard Avoidance (2.2)

## Slide 2: ILP / Pipelining Hazards

## Slide 3: Instruction-Level Parallelism (ILP)
Basic idea: Execute multiple instructions in parallel
  Maximize instruction throughput
Pipelining is a basic and ideal way to realize ILP
Pipelining w stalls
Timeline

## Slide 4: ILP in Practice: Pipelining Hazards
Pipelining hazards
  A situation where (strictly) pipelining the program execution leads to incorrect result.
Causes:
  Limited HW resources: Structural hazard
  Data dependency in program: Data hazard
    Dependency may/may not cause data hazards
  Branch instructions: Branch hazard (next class)
DADD R1, R2, R3
…. (100 insns)
SD R1, O(R4)
DADD R1, R2, R3
SD R1, O(R4)
Dependency & hazards
Dependency but no hazards

## Slide 5: Structural Hazard
Caused by resource conflicts: e.g. registers

## Slide 6: Structural Hazard Avoidance
Stalls
  When a sequence of instructions encounters this hazard, the pipeline will stall one of the instructions until the required unit is available.

## Slide 7: Data Hazard
Data hazard:
  Pipelined execution changes the ordering data are accessed (i.e. read or written).
  Caused by data dependence in program

## Slide 8: Data Hazard

## Slide 9: Data Hazard Avoidance: Forwarding/Stalls
Data hazard:
  When pipeline changes the ordering of read/write access in sequential access.
Stalls
Forwarding

## Slide 10: Data/Name Dependences

## Slide 11: Data Dependence
Data dependence
  Instruction j is data-dependent on instruction i if
    Instruction i produces a result that may be used by instruction j
    Or more generally, operands of instruction i and j overlap
Dependent instructions cannot be executed simultaneously
Notes: Loop-Level Parallelism
  Unroll loop statically or dynamically
  Use SIMD (vector processors and GPUs)

## Slide 12: Data Dependences
Register dependencies
  RAW, WAR, WAW, based on register number
Memory dependencies
  Based on memory address
  This is harder
    Register names known at decode
    Memory addresses not known until execute
SD R1, O(R4)
LD R2, O(R4)
R1 = R2 + R3
R4 = R1 * R4
Notes:   R1 = R2 + R3
  R4 = R1 * R4

## Slide 13: Data Dependencies
RAW: Read-After-Write
  A writes to a location, B reads from the location, therefore B has a RAW dependency on A
  True Dependence
WAR: Write-After-Read
  A reads from a location, B writes to the location, therefore B has a WAR dependency on A
  Anti-Dependence
WAW: Write-After-Write
  A writes to a location, B writes to the location, therefore B has a WAW dependency on A
  Output Dependence
Name dependence
R1 = R2 + R3
R4 = R1 * R4
R1 = R2 + R3
R2 = R3 * R4
R1 = R2 + R3
R1 = R3 * R4

## Slide 14: Impact of Ignoring Dependencies
A: R1 = R2 + R3
B: R4 = R1 * R4
5
-2
9
3
R1
R2
R3
R4
Read-After-Write
7
-2
9
3
7
-2
9
21
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
9
15
7
-2
9
15
B
A
A: R1 = R3 / R4
B: R3 = R2 * R4
Write-After-Read
5
-2
9
3
R1
R2
R3
R4
3
-2
9
3
3
-2
-6
3
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
-6
3
-2
-2
-6
3
A
B
Write-After-Write
A: R1 = R2 + R3
B: R1 = R3 * R4
5
-2
9
3
R1
R2
R3
R4
7
-2
9
3
27
-2
9
3
A
B
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
7
-2
9
3
A
B
Notes: Each is an example of how you will get the wrong results if you reorder two instructions that have a register dependency.

## Slide 15: False Dependences
Name dependences are false dependences
  WAW, WAR
Can be solved by renaming registers
  Assuming there are enough registers

## Slide 16: Eliminating WAR Dependencies
WAR dependencies are from reusing registers
A: R1 = R3 / R4
B: R3 = R2 * R4
5
-2
9
3
R1
R2
R3
R4
3
-2
9
3
3
-2
-6
3
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
-6
3
-2
-2
-6
3
B
A
5
-2
9
3
R1
R2
R3
R4
5
-2
9
3
3
-2
9
3
B
A
4
R5
-6
-6
A: R1 = R3 / R4
B: R5 = R2 * R4
X
With no dependencies, reordering
still produces the correct results
Notes: example shows how using a different architected register removes WAR

## Slide 17: Eliminating WAW Dependencies
WAW dependencies are also from reusing registers
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
27
-2
9
3
B
A
4
R5
4
7
A: R1 = R2 + R3
B: R1 = R3 * R4
5
-2
9
3
R1
R2
R3
R4
7
-2
9
3
27
-2
9
3
A
B
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
7
-2
9
3
A
B
A: R5 = R2 + R3
B: R1 = R3 * R4
X
Same solution works
Notes: example shows similar for WAW

## Slide 18: RAW: Compiler Scheduling & Loop Unrolling

## Slide 19: RAW Hazard Avoidance by Scheduling
Stalling is not enough
Then scheduling! The idea is to schedule or re-order the execution of instructions so that the dependency can go away.
  Compiler approach: compiler scheduling, loop unrolling
  HW approach: CPU OOO (out-of-order execution)
Correctness principle: OOO should execute “correctly”
  To comply with program dependencies
  Same state as if they’re executed one-at-a-time in order
  ISA: “Outside appearance”
  Internally (micro-architecture): “whatever order you want”
    Micro-architecture basically includes everything not explicitly defined in ISA.
Out-of-order execution
Timeline

## Slide 20: ILP in a Loop
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D F4,0(R1)
DADDUI R1,R1,#-8
BNE R1,R2,Loop
RAW
RAW
RAR
RAW
Compile

## Slide 21: Pipeline Stalls
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D F4,0(R1)
DADDUI R1,R1,#-8
BNE R1,R2,Loop
RAW
RAW
RAR
RAW
No stall cycles are needed for RAR; the latencies only apply for RAW!
Notes: DADDUI: double-word add unsigned

## Slide 22: Can Compiler Do Anything?
Stalls are inserted/enforced by HW
Can compiler help?
Pipeline scheduling
  Given the gap/stalls between mutually-dependent instructions, fill it by putting independent instructions
  Re-order the instruction

## Slide 23: Pipeline Scheduling
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4, 0 (R1)
BNE R1,R2,Loop
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
8
DADDUI before ADD, LD, SD!
What about values?
Maintain the correct “outside appearance”.
8
8
8
0
0

## Slide 24: Call for Larger Code Block
Idea: The larger the code block is, the more opportunities there are for scheduling instructions.
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4,8(R1)
BNE R1,R2,Loop

## Slide 25: Loop unrolling: Initial state
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4,8(R1)
BNE R1,R2,Loop
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
for (i=999; i>=0; i=i-2){
x[i] = x[i] + s;
x[i+1] = x[i+1] + s;
}
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
Regular loop
Loop unrolled

## Slide 26: Loop unrolling
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4,8(R1)
BNE R1,R2,Loop
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
for (i=999; i>=0; i=i-2){
x[i] = x[i] + s;
x[i+1] = x[i+1] + s;
}
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
Unscheduled unrolled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop;
L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
-16
Eliminate conditional branch instructions
Scheduled unrolled code:
Loop: L.D F0,0(R1)
L.D F5,-8(R1)
ADD.D F4,F0,F2
ADD.D F9,F5,F2
DADDUI R1,R1,#-16
S.D F4,16(R1)
S.D F9,8(R1)
BNE R1,R2,Loop
More chances for reordering

## Slide 27: Loop unrolling: Outcome
Scheduled code:
Loop: L.D F0,0(R1)
DADDUI R1,R1,#-8
ADD.D F4,F0,F2
stall
stall
S.D F4,8(R1)
BNE R1,R2,Loop
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
for (i=999; i>=0; i=i-2){
x[i] = x[i] + s;
x[i+1] = x[i+1] + s;
}
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop
Scheduled unrolled code:
Loop: L.D F0,0(R1)
L.D F5,-8(R1)
ADD.D F4,F0,F2
ADD.D F9,F5,F2
DADDUI R1,R1,#-16
S.D F4,16(R1)
S.D F9,8(R1)
BNE R1,R2,Loop
Unscheduled code:
Loop: L.D F0,0(R1)
stall
ADD.D F4,F0,F2
stall
stall
S.D F4,0(R1)
DADDUI R1,R1,#-8
stall (integer load latency is 1)
BNE R1,R2,Loop

## Slide 28: Want More Speedup?
Unroll by a factor of 4, 8, …
  # of iterations divisible by the unrolling factor
  Eliminate unnecessary instrs, remove stalls
      Loop:L.D F0,0(R1)
      ADD.D F4,F0,F2
      S.D F4,0(R1) ;drop DADDUI & BNE
      L.D F6,-8(R1)
      ADD.D F8,F6,F2
      S.D F8,-8(R1) ;drop DADDUI & BNE
      L.D F10,-16(R1)
      ADD.D F12,F10,F2
      S.D F12,-16(R1) ;drop DADDUI & BNE
      L.D F14,-24(R1)
      ADD.D F16,F14,F2
      S.D F16,-24(R1)
      DADDUI R1,R1,#-32
      BNE R1,R2,Loop
Limiting infinite unrolling
Limited number of live registers
Code size (increasing time on IF stage)

## Slide 29: Conclude: Pipelining Hazard Avoidance
Basic solution: Stalling pipeline
Structural hazard: forwarding, renaming
Data hazard
  Compiler: compiler scheduling and loop unrolling
  Hw: dynamic scheduling (or out-of-order execution OOO)
Branch hazard
  Branch prediction (next class)
Implementation and application:
  Compiler-based static approaches
    Not so successful outside of scientific applications
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMD processors