## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Branch Hazard Avoidance by Prediction (2.3)
Textbook: 3.3, 3.9, C.2

## Slide 2: Branch Hazard & Prediction (Overview)

## Slide 3: Branch Hazards
Branch instruction is fundamentally hard to execute inside pipeline
  Don’t know which instruction to fetch after the branch
    Branch outcome only known after the EX stage
    Don’t know which instruction to continue before the EX stage.
  And it matters! Approx. 20% of all instructions are branches

## Slide 4: Why Branch is Hard to Pipeline
Cite: http://www.cs.fsu.edu/~hawkes/cda3101lects/chap6/F6.50.gif

## Slide 5: Branch Hazard Avoidance
Stalls (until branch finishes WB)
Predict the branch:
  Fetch/decode on the predicted path
  On EX:
    Option 1: Don’t execute until branch resolved
    Option 2: Execute anyway (speculation)
  Recover from misprediction
    Restart fetch from correct path

## Slide 6: Branch Prediction
Need to know two things
  Direction: Whether the branch is taken or not
  Target: The target address if it is taken
Direct jumps, Function calls
  Direction known (always taken), target easy to compute
Indirect jumps, function returns
  Direction known (always taken), target difficult
Conditional Branches (typically PC-relative)
  Direction difficult to predict, target easy to compute
  If (v == 1){
  A;
  } Else {
  B;
  }
  Foo(){
  B;
  C;
  }
  Main(){
  A;
  Foo();
  D;
  }

## Slide 7: Branch Direction Prediction

## Slide 8: Static Branch Prediction
Direction prediction on conditional branches
  Static: fixed rule, or compiler annotation
  NT: Always predict NT
    easy to implement
    30-40% accuracy … not so good
  T: Always predict T
    60-70% accuracy
  BTFNT (Backward T, Forward NT)
    Going backward is a good sign of loop
    Loops usually have a number of iterations, so this is like always predicting that the loop is taken
  “BEQL” is “branch if equal likely”

## Slide 9: Advanced Branch Prediction
Dynamic branch prediction for direction
  Basic 2-bit predictor
  Two-level predictor
  Tournament predictor
    Combine multiple types of predictors

## Slide 10: One-Bit Branch Predictor
Branch PC (k bits)
Index
Branch history table (BHT) 2^k entries, each of 1 bit
Use this entry to predict this branch:
0: predict not taken
1: predict taken
When branch direction resolved, go back into the table and update entry: 0 if not taken, 1 if taken
Note: we know this before we even fetch the instruction

## Slide 11: One-Bit Branch Predictor (cont’d)
0xDC08: for(i=0; i < 100000; i++)
{
0xDC44: if( ( i % 100) == 0 )
        tick( );
0xDC50: if( (i & 1) == 1)
odd( );
        }
N
T
N
N
T
T
N
T
N
Predict based on what happened the last time.
Correct!
Wrong!
Correct!
Correct!

## Slide 12: One-Bit Branch Predictor: Performance
DC08: TTTTTTTTTTT ... TTTTTTTTTTNTTTTTTTTT …
100,000 iterations
How often is branch outcome != previous outcome?
2 / 100,000
TN
NT
DC44: TTTTT ... TNTTTTT … TNTTTTT …
2 / 100
DC50: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
2 / 2
99.998%
Prediction
Rate
98.0%
0.0%
Each anomaly in a stable pattern results in two mispredictions per loop
Notes: T -> taken N->not taken

## Slide 13: Two Bits are Better Than One
0
1
FSM for Last-Outcome
Prediction
0
1
2
3
FSM for 2bC
(2-bit Counter)
Predict NT
Predict T
Transition on T outcome
Transition on NT outcome

## Slide 14: Performance
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1bC:
2bC:
Only 1 Misprediction per N branches now!
DC08: 99.999% DC44: 99.0%
0
1
2
3
FSM for 2bC
(2-bit Counter)
Checkmark: predict right
Crossmark: predict wrong
Notes: 1bc -> 1 bit predictor , T -> actual outcome of branch taken , N->actual outcome of branch not taken, 0 -> wrong prediction , 1-> correct prediction
2bc (2bit counter) -> 0->1 transition on taken, 1->2 transition on taken(t), finally stays at 3 … , (green -> follow taken arrow(t), red-> follow not taken(n) )

## Slide 15: Performance: How about DC50?
DC50: N T N T N T …
0
1
2
3
FSM for 2bC
(2-bit Counter)
2
T

3
N

2
T

3
N

2
T

3
N

2-bit for DC50?
  Always predict T
  Miss-prediction rate: 50%
Notes: Initially is misprediction, because N is not taken , but state is 3, (observe here 2 , 3 are green so T is tick(\/) here but * is wrong for these states)

## Slide 16: Importance of Branches
98%  99%
  Who cares?
  Actually, it’s 2% misprediction rate  1%
  Half as many mispredictions!
So what?
  If misp rate equals 50%, and 1 in 5 insts is a branch, then number of useful instructions that we can fetch is:
  5*(1 + ½ + (½)2 + (½)3 + … ) = 10
  If we halve the miss rate down to 25%:
  5*(1 + ¾ + (¾)2 + (¾)3 + … ) = 20
  Halving the miss rate doubles the number of useful instructions that we can try to extract ILP from

## Slide 17: Still Not Good Enough
We can live with these
These are good
This is bad!

## Slide 18: The case of Branch at 0xdc50?
Both 1bc and 2bc don’t do well (50% at best)
But it’s still obviously predictable
  Why?: It has a repeating pattern: (NT)*
Patterns are common? (TTNTN)*
Key idea: Remember patterns!
  (NT)* has two patterns:
    NT  N
    TN  T
  Let’s remember both patterns!
Implementation: Having more pred. per branch instruction
  Previously, only one predictor (one PHT entry) per branch
DC50: NTNTNT …
Notes: Assume, for example, that a conditional jump is taken every third time. The branch sequence is 001001001... In this case, entry number 00 in the pattern history table will go to state "strongly taken", indicating that after two zeroes comes a one. Entry number 01 will go to state "strongly not taken", indicating that after 01 comes a 0. The same is the

## Slide 19: Using Two-Level Predictor
A (m, n) two-level branch predictor:
  PHT: Pattern-history table
  PHT Index: Branch PC + shift register (BHR)
  PHT has 2^m predictors, each of n-bit
Different patterns are now handled separately!
  For one target PC, two patterns (NT)* and (TN)* remembered
  By different 2-bit predictors!
Branch PC
Index
T/N
BHR
f
PHT
n
2^m
Notes: Assume, for example, that a conditional jump is taken every third time. The branch sequence is 001001001... In this case, entry number 00 in the pattern history table will go to state "strongly taken", indicating that after two zeroes comes a one. Entry number 01 will go to state "strongly not taken", indicating that after 01 comes a 0. The same is the

## Slide 20: 0xDC50 with two-level predictor
DC50:
T
N
3
T

3
N

3
T

2
N

DC50
Index
NT/TN
f
PHT
n
m
NT:
TN:
BHR
0
1
2
3
3
2
3
1
3
T

N

1
3
T

N

0
…

## Slide 21: Further Improve: Interplay between branches?
Example: related branch conditions
  p = findNode(foo);
  if ( p is parent )
  do something;
  do other stuff; /* may contain more branches */
  if ( p is a child )
  do something else;
Outcome of second
branch is always
opposite of the first
branch
A:
B:

## Slide 22: Other Global Correlations
Testing same/similar conditions
  code might test for NULL before a function call, and the function might test for NULL again
  in some cases it may be faster to recompute a condition rather than save a previous computation in memory and re-load it
  partial correlations: one branch could test for cond1, and another branch could test for cond1 && cond2 (if cond1 is false, then the second branch can be predicted as false)
  multiple correlations: one branch tests cond1, a second tests cond2, and a third tests cond1  cond2 (which can always be predicted if the first two branches are known).

## Slide 23: Global/Local Predictor
Local predictor
  What is the predicted direction of Branch A given the outcomes of previous instances of Branch A?
  Each PHT entry recording the last n outcomes of the branch
Global predictor
  What is the predicted direction of Branch Z given the outcomes of all* previous branches A, B, …, X and Y?
  Each PHT entry recording the outcomes of preceding n branches

## Slide 24: Global/Local predictor implementation
Branch PC
Index
T/N
BHR
f
PHT
n
m
BHR: recent outcomes
  Global: one entry (by Intel)
  Local: multi-entries, one per branch

## Slide 25: Direction Prediction by Tournament Predictor

## Slide 26: Tournament Predictors
No predictor is clearly the best
  Different branches exhibit different behaviors
    Some “constant”, some global, some local
Idea: Let’s have a meta-predictor to predict which predictor will do a better job? 

## Slide 27: Tournament Hybrid Predictors
Pred0 | Pred1 | Meta Update
 |  | ---
 |  | Inc
 |  | Dec
 |  | ---
Pred0
Pred1
Selector
Final Prediction
table of 2-/3-bit counters
If meta-counter MSB = 0,
use pred0 else use pred1

## Slide 28: Common Combinations
Global history + Local history
“Easy” branches + global history
  2bC and gshare
Short history + long history
Many types of behaviors, many combinations

## Slide 29: Branch Prediction Performance
Branch predictor performance

## Slide 30: Examples
Alpha 21264 (RISC): Tournament predictor
  Combines local and global history components with a meta-predictor
Pentium M:
  Hybrid: uses tag-based selection mechanism
  Local component for loops
    It accurately predicts branches of form (TkN)*

## Slide 31: Pentium-M (cont’d)
Special target prediction for indirect branches
  common in object-oriented code (vtables)
  assumes correlation with global history

## Slide 32: Branch Target Prediction

## Slide 33: Target Address Prediction
To maintain pipeline, target addr. needs known right after IF
For direct branch, target only known after ID; too late
For indirect branch, target known after EX/MEM stage; way too late
So, we need a quick-and-dirty predictor for the target addr.
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6
CALL foo | IF | ID | EX | MEM | WB | 
foo |  | IF | ID | EX | MEM | WB

## Slide 34: Branch Target Buffer for CALL/JMP
BTB indexed by instruction address
  We don’t even know if it is a branch!
  If address matches a BTB entry, it is predicted to be a branch
BTB entry tells whether it is taken (direction) and where it goes if taken
BTB takes only the instruction address, so while we fetch one instruction in the IF stage we are predicting where to fetch the next one from
Direction prediction can be factored out into separate table

## Slide 35: Branch Target Buffer

## Slide 36: BTB with Conditional Branch
Situation
The pipeline for instruction predicted to run after a taken branch

## Slide 37: Return Address Stack (RAS) for RET
Function returns are frequent, yet
  Address is difficult to compute (have to wait until EX stage done to know it)
  Address difficult to predict with BTB (function can be called from multiple places)
But return address is actually easy to predict
  It is the address after the last call instruction that we haven’t returned from yet
  Hence the Return Address Stack
Notes: return address stacks are also very simple: they're fixed size stacks of return addresses.
to use a return address stack, we push pc+4 onto the stack when we execute a procedure call instruction. this pushes the return address of the call instruction onto the stack - when the call is finished, it will return to pc+4 of the procedure call instruction. when we execute a return instruction, we pop an address off the stack, and predict that the return instruction will return to the popped address.
since return instructions almost always return to the last procedure call instruction, return address stacks are highly accurate.
remember that return address stacks only generate predictions for return instructions. they don't help at all for procedure call instructions [we use the btb to predict calls].

## Slide 38: Return Address Stack (RAS)
Call pushes return address into the RAS
When a return instruction decoded, pop the predicted return address from RAS
Accurate prediction even w/ small RAS

## Slide 39: Conclusion and reading lists
Dynamic branch direction prediction
  2-bit predictor (Textbook C.2)
  Correlating predictor
    Textbook 3.3
    http://en.wikipedia.org/wiki/Branch_predictor#Global_branch_prediction
  Tournament predictor (Textbook 3.3)
Branch target prediction (Textbook 3.9)
Ack: Prof. Milos’s slides