## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Tomasulo’s Algorithm (2.4)
Textbook: 3.4, 3.5, 3.6, 3.9p

## Slide 2: Tomasulo’s algorithm

## Slide 3: Dynamic Scheduling
ILP: Enable OOO exec. without hazards
  Static scheduling --- by compiler
  Dynamic scheduling --- in hardware
Benefits of dynamic scheduling:
  Portable, no need to recompile every time
  Know runtime info.
    When some dependences unknown at compile time
      e.g. dependency thr. memory references
    Dealing with unpredictable delays, running other code while waiting for cache misses.

## Slide 4: Implementing Dynamic Scheduling
Tomasulo’s Algorithm
  Used in IBM 360/91 (in the 60s)
  Very similar to what is used today
    Almost all modern high-performance processors use a derivative of Tomasulo’s… much of the terminology survives to today.

## Slide 5: A New Stage: Issue Stage
Tomasulo’s pipeline: IF, Issue, EX/MEM, WB
  Slightly different from conventional 5-stage pipeline:
    EX/MEM: merged for both execution and memory access
    Original ID is decomposed into the new issue stage and read-operand operation merged in EX/MEM stage
    Issue stage for structural dependency
    Read-operand for data dependency
  In-order issue, and out-of-order execution /completion

## Slide 6: New Structure: Reservation Station
Between Issue and EX/MEM stage comes a reservation station
RS structure
  It buffers the operands of pending instructions
  RAT (reg alias table): Mapping from reg to RS entry
RS operations
  Upon instruction Issue, pending instr. may rename register specifier to RS entry.
  Upon instruction completion, the result will directly update buffered operand in RS, making it no need to read register.

## Slide 7: Benefits of reservation station
Solve name dependencies that compiler technology can’t
  Have more registers than specified by the ISA
  Temporarily map ISA registers (“logical” or “architected” registers) to the physical registers to avoid overwrites
Handle register renaming across branches (with extended tomasulo algorithm).

## Slide 8: Tomasulo’s Algorithm
Load and store buffers
  Contain data and addresses, act like reservation stations
Top-level design:

## Slide 9: Tomasulo’s algorithm
How to dynamically avoid dependencies at runtime
  Name dependencies are removed by
    Register renaming  reservation station
  True data hazards avoided by proper out-of-order execution
    Tracks when operands are available to satisfy data dependences
  The algorithm extended to avoided control dependencies
    Branch prediction, Hardware speculation
Works in three stages in the pipeline.
  Issue, EX/MEM, WB

## Slide 10: Issue (1)
  Get next instruction from instruction queue.
  Find a free reservation station for it (if none are free, stall until one is)
  Read operands that are in the registers
  If the operand is not in the register, find which reservation station will produce it
  In effect, this step renames registers (reservation station IDs are “temporary” names)

## Slide 11: Issue (2)
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
Instruction Buffers
0
1
0
0
F2=F4+F1
Adder
FP-Cmplx
A1 (1)
A2 (2)
A3 (3)
C1 (4)
C2 (5)
F1
F2
F3
F4
RAT
3.141593
-1.00000
2.718282
0.707107
F1
F2
F3
F4
Reg File
0.7071
p
To-Do list (from last slide):
Get next inst from IB’s
Find free reservation station
Read operands from RF
Record source of other operands
Update source mapping (RAT)
1.
2.
3.
F1=F2/F3
2.718
(1)
4

## Slide 12: Issue (2)
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
Instruction Buffers
0
1
0
0
F2=F4+F1
Adder
FP-Cmplx
A1 (1)
A2 (2)
A3 (3)
C1 (4)
C2 (5)
F1
F2
F3
F4
RAT
3.141593
-1.00000
2.718282
0.707107
F1
F2
F3
F4
Reg File
0.7071
p
To-Do list (from last slide):
Get next inst from IB’s
Find free reservation station
Read operands from RF
Record source of other operands
Update source mapping (RAT)
1.
2.
3.
F1=F2/F3
2.718
(1)
F4=F1-F2
F1=F2+F3
(4)
(1)
(1)
2.718

## Slide 13: Execute (1)
  Monitor results as they are produced
  Put a result into all reservation stations waiting for it (missing source operand)
  When all operands available for an instruction, it is ready for execution
  More than 1 instrs ready for one functional unit?
    Pick one instruction, based on some heuristic.
    Except for load/store: Load/Store must be done in the proper order to avoid hazards through memory (not covered)

## Slide 14: Execute (2)
F2=F4+F1
F4=F1-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
A1 (1)
A2 (2)
A3 (3)
C1 (4)
C2 (5)
0.7071
p
(4)
(1)
(1)
2.718
To-Do list (from last slide):
Monitor results from ALUs
Capture matching operands
Compete for ALUs
2.718
(1)
F2=F4+F1
(1) 3.8487
3.8487
3.8487
3.8487

## Slide 15: >1 ready inst for the same unit
F2=F4+F1
F4=F3-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
A1 (1)
A2 (2)
A3 (3)
C1 (4)
C2 (5)
0.7071
p
2.718
(1)
(1)
2.718
2.718
(1)
F2=F4+F1
(1) 3.8487
3.8487
3.8487
3.8487
Common heuristic: oldest first
Optimal is impossible:
Precedence constrained scheduling
problem is NP-complete [GJ,p239]
… and that assumes you have
access to the entire graph
You can do whatever: it only
affects performance, not correctness

## Slide 16: Write Result (1)
  When result is computed, make it available on the “common data bus” (CDB), where waiting reservation stations can pick it up
  Stores write to memory
  Result stored in the register file
  This step frees the reservation station
  For our register renaming, this recycles the temporary name (future instructions can again find the value in the actual register, until it is renamed again)

## Slide 17: Write Result (2)
Only update RAT
(and RF) if RAT still
contains your mapping! (Prevent WAW hazard)
0
0
3.8486994
F4=F1-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
A1 (1)
A2 (2)
A3 (3)
C1 (4)
C2 (5)
(4)
2.718
To-Do list (from last slide):
Broadcast on CDB
Writeback to RF
Update Mapping
Free reservation station
2.718
3.141593
-1.00000
2.718282
0.707107
F1
F2
F3
F4
Reg File
3
1
0
2
F1
F2
F3
F4
RAT
(1)
(1)
(1)
F2=F4+F1
0.7071
p
(1) 0.7071+p
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
1.
2.
3.
F2 = F4 + F1
0.
3.8487
3.8487
3.8487
X
Notes: If instruction (4) finishes first, it can not update the RAT and register file, because it is instruction (3) in the RAT entry and it is (3) that should update reg file when it finishes.
Thus eventually, result of (3) will be rewritten to F1@RegFile, and result of (4) will be used for instruction (2)

## Slide 18: Tomasulo’s Algorithm: Load/Store
The reservation stations take care of RAW dependences through registers.
Dependences also possible through memory
  Loads/stores not reordered in original IBM 360
  We’ll talk about how to do load-store reordering later

## Slide 19: Detailed Example: Cycle 0
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | N |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) |  |  | 
2. | L.D F2, 45(R3) |  |  | 
3. | MUL.D F0, F2, F4 |  |  | 
4. | SUB.D F8, F2, F6 |  |  | 
5. | DIV.D F10,F0, F6 |  |  | 
6. | ADD.D F6, F8, F2 |  |  | 
The ’busy’ tag says RS line is occupied. Also says the instruction is in IS/EX, but not IF/WB

## Slide 20: Detailed Example: Cycle 1
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | Y | LD |  |  |  |  | 34+[R2]
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | N |  |  |  |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 |  | 
2. | L.D F2, 45(R3) |  |  | 
3. | MUL.D F0, F2, F4 |  |  | 
4. | SUB.D F8, F2, F6 |  |  | 
5. | DIV.D F10,F0, F6 |  |  | 
6. | ADD.D F6, F8, F2 |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | F2 | F4 | LD1 | F8 | F10 | F12 | F14

## Slide 21: Detailed Example: Cycle 2
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | Y | LD |  |  |  |  | 34+[R2]
LD2 | Y | LD |  |  |  |  | 45+[R3]
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | N |  |  |  |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 
2. | L.D F2, 45(R3) | 2 |  | 
3. | MUL.D F0, F2, F4 |  |  | 
4. | SUB.D F8, F2, F6 |  |  | 
5. | DIV.D F10,F0, F6 |  |  | 
6. | ADD.D F6, F8, F2 |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | LD2 | F4 | LD1 | F8 | F10 | F12 | F14

## Slide 22: Detailed Example: Cycle 3
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | Y | LD |  |  |  |  | 34+[R2]
LD2 | Y | LD |  |  |  |  | 45+[R3]
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL |  | [F4] | LD2 |  | 
ML2 | N |  |  |  |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 
2. | L.D F2, 45(R3) | 2 | 3 | 
3. | MUL.D F0, F2, F4 | 3 |  | 
4. | SUB.D F8, F2, F6 |  |  | 
5. | DIV.D F10,F0, F6 |  |  | 
6. | ADD.D F6, F8, F2 |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | LD2 | F4 | LD1 | F8 | F10 | F12 | F14

## Slide 23: Detailed Example: Cycle 4
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | Y | LD |  |  |  |  | 45+[R3]
AD1 | Y | SB |  | [F6] | LD2 |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL |  | [F4] | LD2 |  | 
ML2 | N |  |  |  |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 
3. | MUL.D F0, F2, F4 | 3 |  | 
4. | SUB.D F8, F2, F6 | 4 |  | 
5. | DIV.D F10,F0, F6 |  |  | 
6. | ADD.D F6, F8, F2 |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | LD2 | F4 | F6 | AD1 | F10 | F12 | F14

## Slide 24: Detailed Example: Cycle 5
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | Y | SB | [F2] | [F6] |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 |  | 
4. | SUB.D F8, F2, F6 | 4 |  | 
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | F6 | AD1 | ML2 | F12 | F14

## Slide 25: Detailed Example: Cycle 6
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | Y | SB | [F2] | [F6] |  |  | 
AD2 | Y | AD |  | [F2] | AD1 |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | AD2 | AD1 | ML2 | F12 | F14

## Slide 26: Detailed Example: Cycle 7
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | Y | SB | [F2] | [F6] |  |  | 
AD2 | Y | AD |  | [F2] | AD1 |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | AD2 | AD1 | ML2 | F12 | F14

## Slide 27: Detailed Example: Cycle 8
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | Y | AD | [F8] | [F2] |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | AD2 | F8 | ML2 | F12 | F14

## Slide 28: Detailed Example: Cycle 9
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | Y | AD | [F8] | [F2] |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 | 9 | 
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | AD2 | F8 | ML2 | F12 | F14

## Slide 29: Detailed Example: Cycle 11
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | Y | MUL | [F2] | [F4] |  |  | 
ML2 | Y | DIV |  | [F6] | ML1 |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 | 9 | 11
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
ML1 | F2 | F4 | F6 | F8 | ML2 | F12 | F14

## Slide 30: Detailed Example: Cycle 16
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | Y | DIV | [F0] | [F6] |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 16
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 |  | 
6. | ADD.D F6, F8, F2 | 6 | 9 | 11
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | F2 | F4 | F6 | F8 | ML2 | F12 | F14

## Slide 31: Detailed Example: Cycle 17
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | Y | DIV | [F0] | [F6] |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 16
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 | 17 | 
6. | ADD.D F6, F8, F2 | 6 | 9 | 11
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | F2 | F4 | F6 | F8 | ML2 | F12 | F14

## Slide 32: Detailed Example: Cycle 57 (final)
Reservation Stations
Register Status:
Cycle:
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
R2 is 100
R3 is 200
F4 is 2.5
 | Busy | Op | Vj | Vk | Qj | Qk | A
LD1 | N |  |  |  |  |  | 
LD2 | N |  |  |  |  |  | 
AD1 | N |  |  |  |  |  | 
AD2 | N |  |  |  |  |  | 
AD3 | N |  |  |  |  |  | 
ML1 | N |  |  |  |  |  | 
ML2 | Y | DIV | [F0] | [F6] |  |  | 
 | Instruction | Is | Ex | Wr
1. | L.D F6, 34(R2) | 1 | 2 | 4
2. | L.D F2, 45(R3) | 2 | 3 | 5
3. | MUL.D F0, F2, F4 | 3 | 6 | 16
4. | SUB.D F8, F2, F6 | 4 | 6 | 8
5. | DIV.D F10,F0, F6 | 5 | 17 | 57
6. | ADD.D F6, F8, F2 | 6 | 9 | 11
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14
Out-of-order Ex/WB?
Solved by HW Speculation!

## Slide 33: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) |  |  |  | 
2. | L.D F2, 45(R3) |  |  |  | 
3. | MUL.D F0, F2, F4 |  |  |  | 
4. | SUB.D F8, F2, F6 |  |  |  | 
5. | DIV.D F10,F0, F6 |  |  |  | 
6. | ADD.D F6, F8, F2 |  |  |  | 

## Slide 34: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) | 1 | 2 | 4 | 
2. | L.D F2, 45(R3) | 2 | 3 | 5 | 
3. | MUL.D F0, F2, F4 | 3 |  |  | 
4. | SUB.D F8, F2, F6 |  |  |  | 
5. | DIV.D F10,F0, F6 |  |  |  | 
6. | ADD.D F6, F8, F2 |  |  |  | 

## Slide 35: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) | 1 | 2 | 4 | 
2. | L.D F2, 45(R3) | 2 | 3 | 5 | 
3. | MUL.D F0, F2, F4 | 3 | 6 | 16 | 
4. | SUB.D F8, F2, F6 | 4 |  |  | 
5. | DIV.D F10,F0, F6 |  |  |  | 
6. | ADD.D F6, F8, F2 |  |  |  | 

## Slide 36: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) | 1 | 2 | 4 | 
2. | L.D F2, 45(R3) | 2 | 3 | 5 | 
3. | MUL.D F0, F2, F4 | 3 | 6 | 16 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8 | 
5. | DIV.D F10,F0, F6 | 5 |  |  | 
6. | ADD.D F6, F8, F2 |  |  |  | 

## Slide 37: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) | 1 | 2 | 4 | 
2. | L.D F2, 45(R3) | 2 | 3 | 5 | 
3. | MUL.D F0, F2, F4 | 3 | 6 | 16 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8 | 
5. | DIV.D F10,F0, F6 | 5 | 17 | 57 | 
6. | ADD.D F6, F8, F2 | 6 |  |  | 

## Slide 38: Timing Example
Simplified version to track only timing
  Much faster to do by hand (for exams and such)
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) | 1 | 2 | 4 | 
2. | L.D F2, 45(R3) | 2 | 3 | 5 | 
3. | MUL.D F0, F2, F4 | 3 | 6 | 16 | 
4. | SUB.D F8, F2, F6 | 4 | 6 | 8 | 
5. | DIV.D F10,F0, F6 | 5 | 17 | 57 | 
6. | ADD.D F6, F8, F2 | 6 | 9 | 11 | 

## Slide 39: Timing Example (2)
Now let’s assume that we can’t broadcast and select in the same cycle
Load: 2 cycles
Add: 2 cycles
Mult: 10 cycles
Divide: 40 cycles
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) |  |  |  | 
2. | L.D F2, 45(R3) |  |  |  | 
3. | MUL.D F0, F2, F4 |  |  |  | 
4. | SUB.D F8, F2, F6 |  |  |  | 
5. | DIV.D F10,F0, F6 |  |  |  | 
6. | ADD.D F6, F8, F2 |  |  |  | 

## Slide 40: Conflict Example
Careful: keep track of all the resources
 | Instruction | Is | Ex | Wr | Comment
1. | L.D F6, 34(R2) |  |  |  | 
2. | ADD.D F2, F0, F10 |  |  |  | 
3. | SUB.D F0, F6, F4 |  |  |  | 
4. | MUL.D F8, F2, F6 |  |  |  | 
5. | L.D F10,28(R4) |  |  |  | 
6. | ADD.D F6, F4, F12 |  |  |  | 
Load: 2 cycles
Add: 1 cycles
Mult: 4 cycles
Divide: 40 cycles

## Slide 41: Hardware Speculation

## Slide 42: Hardware Speculation
Use cases: Hardware Speculation can undo inconsistent data produced by
  OOO execution
  Branch misprediction
Key design: to distinguish commit operations in WB stage
  Execute/complete speculatively (e.g. out-of-order).
  But commit (e.g. in order) in the WB stage
    Commit means update the register files and mapping.
    For out-of-order instruction, simply skip commit.
  The same for misprediction.
Implementation: Reorder buffer(ROB)
  Using ROB to store all instrs completed but uncommitted.
  ROB provides additional registers
    The same to that RS provides addition registers in Tomasolu.
Notes:   Dynamic scheduling
    Enable OOO execution of instructions across branch boundaries
A: i = i+1;
B: if(i==0){
C: i = i-1;
}

## Slide 43: ROB in multi-issue CPU
How to maintain the illusion of sequentiality?
5s
30s
5s
5s
Hands toll-booth
agent a $100 bill;
takes a while to
count the change
One-at-a-time = 45s
With a “4-Issue” Toll Booth
L1
L2
L3
L4
OOO = 30s
Notes: OOO = Out of Order

## Slide 44: Operating ROB
Add to ROB:
  Upon completion of an instruction
Remove from ROB:
  Upon branch instr. resolved
  That’s when a misprediction can be confirmed:
    Correct prediction: Commit the instruction
    Misprediction: Simply clear the instruction from ROB
Instruction commit:
  Update the register file

## Slide 45: Conclusion and further readings
Dynamic scheduling, Tomasulo’s algorithm
  Textbook 3.4
  Textbook 3.5
Hardware speculation
  Textbook 3.6, 3.9(partially)
Ack: Prof. Milos’s slides, Copyright © 2012, Elsevier Inc