## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Multi-issue processor and SIMD (2.5)
Textbook: 3.7, 3.9, 3.12, 4

## Slide 2: Multi-issue processor

## Slide 3: Example: Toll Booth
A
B
C
D
Caravanning on a trip, must stay in
order to prevent losing anyone
When we get to the toll, everyone gets
in the same lane to stay in order
This works… but it’s slow. Everyone has to
wait for D to get through the toll booth
Lane 1
Lane 2
Before Toll Booth
After Toll Booth
You Didn’t
See That…
Go through two at a time
(in parallel)

## Slide 4: Multi-issue processor
To achieve CPI < 1
  Multiple functional units: adder, multiplier, FP units, mem-access, etc
  Can issue/complete multiple instructions per clock
Superscalar processor
  Varying number of instrs to issue per clock
  Static scheduled superscalar: In-order EX
  Dynamic scheduled superscalar: Out-of-order EX

## Slide 5: VLIW Processors
VLIW processor:
  Fixed number of instrs to issue per clock
  In-order EX: static scheduled
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Enough parallelism in code to fill available slots

## Slide 6: Multi-issue processor: Towards CPI < 1

## Slide 7: Speculation: HW vs SW
HW speculation: pros
  Runtime behavior is unpredictable at compile time
    Disambiguate memory reference
    Branch predictions
  No bookkeeping code
    Required by ambitious SW speculation
SW speculation: pros
  Have global view: be able to see further in code seq.
  Less complexity in HW

## Slide 8: High-Bandwidth Instruction Stream
It needs to deliver a high-bandwidth instruction stream.
  4-8 instruction per cycle.
Fetch (IF) efficiently:
  Fetching branches: BTB, RAS
Advanced speculation

## Slide 9
Ack: Prof. Rajeev Balasubramonian
Register Renaming with ROB
Extra RF used to rename register
Avoid hazards by naming dep.: WAW/WAR
Simple heuristic: always rename it!

## Slide 10: HW Multithreading

## Slide 11: HW multithreading: Concept
HW multithreading for a single processor
  Different from multi-processing
  Different from SW threads
HW multi-threading
Demo: Hyper-threading by Intel
physical processor ids
# physical cores per processors
virtual core ids (Hw Threads)
Notes: There is one package of CPU (physical ID), two cores(hardware level), 4 HW threads => each core has 2 HW threads
HW thread is single pipeline

## Slide 12: HW multithreading: Pros
Multithreading share resources
  Increase of threads will not increase HW resources
  Thus, HW multithreading can hide stalls due to cache misses and memory accesses.

## Slide 13: HW multithreading: Cons
Still there are private states per thread
  Private thread state: PC, register files, renaming tables, page tables (if running dedicated program)
  Private states need to be saved/loaded every-time there is a switch between threads.

## Slide 14: Scheduling: How to switch threads
CMT: coarse-grained multi-threading
  Switch whenever the current thread has a (long) stall
  : need to flush pipeline upon thread switch (branch pred.)
FMT: fine-grained multi-threading
  Switch every clock cycle
  Scheduling in round-robin and to non-stalled threads.
  : be able to handle both long and short stalls
  : no empty cycles (i.e. all slots are empty on that cycle)
  : longer latency for non-stalling threads (more switches)
Notes: Because CMT issues instruction from a single thread, upon switching it may need to flush all instructions in progress in the current pipeline. In other words, not every time it can switch, but only when all instructions in the current pipeline finishes!!!

## Slide 15: Scheduling: How to switch threads
SMT: Simultaneous multi-threading
  A variant of FMT on multi-issue, dynamic scheduled processor.
  Reg renaming and dynamic scheduling allows multiple independent threads to execute
In essence, SMT converts TLP into ILP
  SMT is called Hyper-threading in Intel processors

## Slide 16: Multithreading
T1
T1
T2
T1
T3
T2
T4
Partitioned assembly code
C program
Stall!
Stall on T1
Notes: X axis is referring to different functional units

## Slide 17: DLP in Vector, SIMD, GPU

## Slide 18: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  matrix-oriented scientific computing
  media-oriented image and sound processors
SIMD is more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction

## Slide 19: SIMD Parallelism
Three SIMD variations
  Vector architectures: many pipelined ops
  SIMD extensions: simu. data parallel ops, media app.,
  Graphics Processor Units (GPUs): display, massive number of small threads.
For x86 processors:
  Expect two additional cores per chip per year
  SIMD width to double every four years
  Potential speedup from SIMD to be twice that from MIMD!
    Intel AVX-128, AVX-256, etc
Introduction

## Slide 20: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 21: Sparse Data by Scatter-Gather
Scatter-and-gather supports moving
  Between compressed and normal representations.
  Between index and expanded data forms.
Consider the case of sparse vectors (A[] is indexed by another vector):
for (i = 0; i < n; i=i+1)
A[K[i]] = A[K[i]] + C[M[i]];
Use index vector:
LV Vk, Rk ;load K
LVI Va, (Ra+Vk) ;load A[K[]]
LV Vm, Rm ;load M
LVI Vc, (Rc+Vm) ;load C[M[]]
ADDVV.D Va, Va, Vc ;add them
SVI (Ra+Vk), Va ;store A[K[]]
Vector Architectures
Gather: from sparse to dense form
Scatter: from dense to sparse form
sparse
dense
Notes: LV Vk Rk: Rk is regular register storing address of K[0], while Vk is a vector register of n elements

## Slide 22: SIMD Extensions
Media applications operate on data types narrower than the native 32-bit word.
  Example: 8 bit for each color (GRB)
Limitations, compared to vector instructions:
  Fixed number of operands encoded in op code
  No sophisticated addressing modes (scatter-gather)
SIMD Instruction Set Extensions for Multimedia

## Slide 23: SIMD Implementations
Implementations:
  Intel MMX (1996)
    MMX-64: Eight 8-bit integer ops or four 16-bit integer ops
  Streaming SIMD Extensions (SSE) (1999)
    SSE-128: Eight 16-bit integer ops, Four 32-bit integer/fp ops or two 64-bit integer/fp ops
  Advanced Vector Extensions (2010)
    AVX-256: Four 64-bit integer/fp ops
    AVX-512 (2013)
  Operands must be consecutive and aligned memory locations
SIMD Instruction Set Extensions for Multimedia

## Slide 24: Graphical Processing Units
Given the hardware invested to do graphics well, how to improve performance of a wider range of applications?
Basic idea:
  Heterogeneous execution model
    CPU is the host, GPU is the device
  Develop a C-like programming language for GPU
  Unify all forms of GPU parallelism as CUDA thread
  Programming model is “Single Instruction Multiple Thread”
Graphical Processing Units

## Slide 25: NVIDIA GPU Architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor
Graphical Processing Units

## Slide 26: Threads and Blocks
A thread is associated with each data element
Threads are organized into blocks
Blocks are organized into a grid
Graphical Processing Units
Notes: R(registers) - > threads(T) -> Block(B) -> G(GPU) i.e., set of regsiters form thread

## Slide 27: Example
Multiply two vectors of length 8192
  Code that works over all elements is the grid
  Thread blocks break this down into manageable sizes
    512 threads per block
  SIMD instruction executes 32 elements at a time
  Thus grid size = 16 blocks
  Block is analogous to a strip-mined vector loop with vector length of 32
  Block is assigned to a multithreaded SIMD processor by the thread block scheduler
  Current-generation GPUs (Fermi) have 7-15 multithreaded SIMD processors
Graphical Processing Units

## Slide 28: SIMD/GPU Hardware Model
Threads of SIMD instructions
  Each has its own PC
  Thread scheduler uses scoreboard to dispatch
    GPU HW, not OS, handles thread management
  No data dependencies between threads!
  Keeps track of up to 48 threads of SIMD instructions
    Hides memory latency
Within each SIMD processor:
  32 SIMD lanes
  Wide and shallow compared to vector CPU
Graphical Processing Units

## Slide 29: SIMD/GPU : Example
NVIDIA GPU has 32,768 registers
  Divided into lanes
    There’re 16 physical SIMD lanes, each of 2048 registers
  Each SIMD thread accesses one lane, with up to:
    64 vector registers of 32 32-bit elements
    32 vector registers of 32 64-bit elements
Graphical Processing Units

## Slide 30: NVIDIA GPU Memory Structures
Private memory: SIMD Lane, off-chip DRAM
  Contains stack frame, private variables, etc
Local memory: multithreaded SIMD processor
  Shared by SIMD lanes / threads within a block
Shared GPU memory:
  Host CPU can read and write GPU memory
Graphical Processing Units

## Slide 31: Conclusion and reading lists
Multi-issue processors (Textbook 3.7, 3.9)
Multi-threading (Textbook 3.12)
DLP in Vector, SIMD, GPU (Textbook 4)