## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Virtual Memory (3.3)
Textbook: B.4, B.5, 2.4

## Slide 2: Virtual Memory

## Slide 3: Views of Memory
Real machines have different memory sizes
  640MB? A few GB?
  (An average laptop: 2GB)
Programmer doesn’t want to be bothered
  Do you think, “oh, this computer only has 128MB so I’ll write my code this way…”
  What happens if you run on a different machine?

## Slide 4: Programmer’s View
Example 32-bit memory layout
  Segments
Independent of the actual memory there is
  You don’t need to buy a machine with 4GB memory to run programs requiring 4GB space.
Kernel
Text
Data
Heap
Stack
0-2GB
4GB
A.K.A. Virtual Addresses
Notes: Text seg. store program code
Data seg. store data
Heap stores global data
Stack stores local variable.

## Slide 5: Programmer’s View (2)
Multi-programming:
  Each process runs in an exclusive addr. space.
  Context switches btwn processes at any time
Isolation btwn different addr. spaces
Kernel
Text
Data
Heap
Stack
Kernel
Text
Data
Heap
Stack
Kernel
Text
Data
Heap
Stack
Notes: Text seg. store program code
Data seg. store data
Heap stores global data
Stack stores local variable.

## Slide 6: CPU’s View
At some point, the CPU is going to have to load-from/store-to memory… all it has to know is the real, A.K.A. physical memory
The physical space
is often not equal to 4GB
Multiple virt. spaces but only one physical memory.
And physical space is almost never
4GB per process

## Slide 7: Connecting virt./phys. memories: Pages
Divide memory into pages
Pages are nothing more than fixed sized and aligned regions of memory
  Typical size: 4KB/page (but not always)
0-4095
4096-8191
8192-12287
12288-16383
…
Page 0
Page 1
Page 2
Page 3

## Slide 8: Page Table
Map from virtual addresses to physical locations
0K
4K
8K
12K
Virtual
Addresses
0K
4K
8K
12K
16K
20K
24K
28K
Physical
Addresses
“Physical Location” may
include hard-disk
Page Table implements
this VP mapping
Entry includes permissions (e.g., read-only)

## Slide 9: Multiple Page Tables
0K
4K
8K
12K
0K
4K
8K
12K
16K
20K
24K
28K
0K
4K
8K
12K
Physical Memory

## Slide 10: Address Translation Mechanism
Virtual Address
Virtual Page Number
Page Offset
Page
Table
Main
Memory
Physical
Address
0xFC51908B
0x00152
0xFC519
0x0015208B
Instructions
(CPU/$)

## Slide 11: Page Table Internals: Simple PT
Flat organization
  One entry per page
  Entry contains physical page number (PPN) or indicates page is on disk or invalid
  Also meta-data (e.g., permissions, dirtiness, etc.)
One entry per page

## Slide 12: Simple Page Table Size?
Assume:
  32-bit address space for process
  4KB page
  Page table entry: 8 bytes
Page table size?
Notes: print

## Slide 13: Simple Page Table Size?
Assume:
  32-bit address space for process
  4KB page
  Page table entry: 8 bytes
Page table size?
  8 * 232 / 4 * 1024
  = 223 = 8MB
What if the program only uses 4MB of memory?
What if the page size is 1MB?
What if 64-bit address space?
Notes: 2^32 words . Each word stores a byte of information.

## Slide 14: Multi-Level Page Tables
Level 1
Level 2
Page Offset
Physical Page Number
Virtual Page Number
X
Unused addr. space will not have level-2 page table

## Slide 15: Multi-Level Page Table Size?
Assume:
  32-bit address space for process, 4KB page
  1st level uses 8 bits of indexing, 2nd level uses 12 bits
  Page table entry: 8 bytes
First-level page table size?
  Size? 8 * 28 = 211 = 2KB
  28 entries also mean one L1 can point to up to 28 L2 PTs
Second-level page table size?
  8 * 212 = 215 = 32KB
  212 entries also mean one L2 can point to 212=4096 pages
What if the program only uses 4MB of memory?
  4MB can fit in one second-level PT (4MB=1000 pages < 4000 pages)
  It will need 1 L1 and 1 L2 page tables.
  Total page-table size: 2KB + 1 * 32KB=34KB
Notes: Print, and failed before! need your attention!

## Slide 16: Multi-Level Page Table Size?
Assume:
  32-bit address space for process, 4KB page
  1st level uses 5 bits of indexing, 2nd uses 6 bits, 3rd uses 9 bits
  Page table entry: 8 bytes
First-level page table size?
  8 * 25 = 28 = 256bytes
  25 entries also mean one L1 can point to up to 25 L2 PTs
Second-level page table size?
  8 * 26 = 29 = 512bytes
  26 entries also mean one L2 can point to 26 L3 PTs
Third-level page table size?
  8 * 29 = 212 = 4KB
  29 entries also mean one L3 can point to 29 pages = 2MB
What if the program only uses 4MB of memory?
  It will need 1 L1, 1 L2 and 2 L3 page tables.
  Total page-table size: 256 + 1 * 512 + 2 * 4KB < 9KB
Notes: print

## Slide 17: Choosing a Page Size
Small pages result in larger page table
Small page leads to less fragmentation
  Big page likely to have more bytes unused
Large pages allow efficient transfer to/from disk
  vs. many small transfers
  Like downloading from Internet

## Slide 18: TLB

## Slide 19: Page Table’s Impact on Performance
Every load/store needs to access memory twice!
  “LD R1 0xFC51908B”
  First mem. access: translating 0xFC51908B to 0x0015208B
    This could be more than one memory access (Why?)
  Second mem. access: load data at 0x0015208B from physical mem.
Even worse, every IF (instruction fetch) requires translation of the PC!
Idea: cache the page table!

## Slide 20: TLB: Cached Page Translations
TLB: a cache storing address translations
  TLB = Translation Look-aside Buffer
0K
4K
8K
12K
Virtual
Addresses
0K
4K
8K
12K
16K
20K
24K
28K
Physical
Addresses
8
16
0
20
4
4
12
X
VPN 8
PPN 16

## Slide 21: What if there is a TLB miss?
Option 1: Hardware TLB miss handling (x86)
  Hardware register keeps page table location
  Hardware knows how to read page table
    Note: can be complex, e.g. if hierarchical page table
  TLB miss stalls instruction until translation found
Option 2: Software TLB miss handling
  Raise exception on TLB miss
  Software TLB miss handler in OS
    Finds translation (can use any page table structure)
    Writes translation into TLB (need special privileged instruction for this)
  Retry instruction (hopefully now a TLB hit)

## Slide 22: TLB Design: Yet Another Cache
Used to be fully-associative
  Any mapping can be kept in any TLB entry
  Check all entries on each access
  For low latency, this means few entries
  However, each entry is for a whole page
  Ex. 32-entry TLB, 4KB page… how big of working set while avoiding TLB misses?
If many misses:
  Increase TLB size (latency problems)
  Increase page size (fragmenation problems)

## Slide 23: TLB Design: Yet Another Cache
Programs getting bigger
  Larger working set  more pages active  need for TLB to remember more mappings
New processors include larger, but set-associative TLBs
  Mapping can go into a specific part of the TLB
  Use lowest bits of VPN to determine where it can go
Some also include multi-level TLBs (L1/L2)
  If we don’t find mapping in L1, check L2, then memory
  L1 small for speed, L2 larger to improve hit rate

## Slide 24: Process Changes
After context switch TLB content no longer valid!
  Add process ID to translation
8
28
4
20
0
32
12
36
0
1
1
0
4
52
0
16
12
8
8
44
0
0
1
1
PID:0
VPN:8
PPN: 28
PID:1
VPN:8
PPN: 44
Only flush parts of TLB when recycling PIDs

## Slide 25: Conclusion and reading lists
Virtual memory: B.4, B.5, 2.4
Memory protection: 2.4
Virtual machine: 2.5
Ack: Prof. Milos’s slides
Copyright © 2012, Elsevier Inc. All rights reserved.