## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Cache (3.2)
Textbook: 2.1, 2.2, B.1, B.2, B.3

## Slide 2: Cache: What and Why

## Slide 3: Memory hierarchy
Memory hierarchy
  Entire address space into the largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it
  Fast memory technology is more expensive per bit than slower memory
Working:
  Data is not found in the higher-level storage, a miss occurs.
  Fetch data from lower level in hierarchy, incurring a higher latency reference
Why it works:
  Temporal and spatial locality ensures that nearly all references can be found in smaller memories

## Slide 4: Memory/storage hierarchy
Register File
Instruction Cache
Data Cache
L2 Cache
L3 Cache
Main Memory
Disk
Row buffer
SRAM Cache
Bypass Network
10TB/10ms
Speed +/ Capacity -
ITLB
DTLB
Chip
CPU core
Motherboard
IO bus
Memory bus
Capacity +/Speed -
10GB/100ns
1MB/20ns
256 KB/10ns
64 KB/1ns
1000 bytes/100ps(10−12 sec)
Translation lookaside buffer

## Slide 5: Why Cache?
Memory latency is long!
  60-100ns not uncommon
  It’s too long, from CPU’s perspective:
    2GHz CPU  0.5ns / cycle
    100ns memory  200 CPU cycles (idling wo/ cache)!
Memory wall: memory latency is improved slower than CPU speed!

## Slide 6: Why Cache?(2) CPU-mem perf. gap
Introduction

## Slide 7: Why Cache?(3)
Multi-core processors calls for higher memory bandwidth
  Required mem bandwidth increases with # core
  Example: Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
Cache is needed!

## Slide 8: Cache basics

## Slide 9: Cache: Optimizing memory access
Fast (but small) memory close to processor
Data granularity
  Word: finest granularity memory data is addressed
    32 bits
  Block: the granularity data is transferred from memory
    between 4096 bytes and 32KB
When a word referenced
  If in cache, use cache instead of memory
  If not in cache, bring entire block (of words) into cache

## Slide 10: Cache structure
Cache consists of block-sized lines
  A line of multiple words
  Line size typically power of two: 16-128 bytes
Example
  Assume block size is 256=28 bytes
    Lowest eight bits determine offset within block
  Read data at address A=0x7fffa3f4
Word address: | Line address | Offset
7 f f f a 3
f 4

## Slide 11: Cache design
Important decisions
  Placement: where in the cache can a block go?
  Replacement: what to kick out to make room in cache?
  Write policy: What do we do about stores?

## Slide 12: 1) Cache placement
Placement:
  How to map memory block to cache line?
Direct map => a block to only one line
Associative
  Fully associative => a block to all lines
  N-way set associative:
    N-way set: a group of N lines
    => one block to a set of N lines
  N = 1 => Direct-map
  N = C (total # cache lines) => Fully associative
Introduction

## Slide 13: Direct Mapped Cache
Word address: | Tag | Index | Offset
Which part of cache block?
To which line can it go? (3 bits)
Cache Line #
0
1
2
3
4
5
6
7
Cache has 8 lines, need 3 bits that tell us which line to go
101

## Slide 14: 2-Way Set Associative Cache
Address: | Tag | Index | Offset
Which part of cache block?
To which line can it go? (2 bits)
Cache Line #
0
1
2
3
4
5
6
7
Cache has 8 lines, a block can go to one of two lines, so we have 4 sets of 2 lines each
10
Set 0
Set 1
Set 3
Set 2
Need 2 bits to tell us to which of the 4 sets to go

## Slide 15: Fully Associative Cache
Address: | Tag | Offset
Which part of cache block?
Cache Line #
0
1
2
3
4
5
6
7
Block can go anywhere!
No bits needed to tell us where it can go

## Slide 16: 2) Cache replacement
Need a free line to insert new block (for set-associative cache)
  Which block should we kick out?
Several strategies
  Random (randomly selected line)
  FIFO (line that has been in cache the longest)
  LRU (least recently used line)
  LRU Approximations: NMRU

## Slide 17: Implementing LRU
Have LRU counter for each line in a set
When line accessed (cache hit)
  Get old value X of its counter
  Set its counter to max value
  For every other line in the set
    If counter larger than X, decrement it
When replacement needed (cache miss)
  Select line whose counter is 0

## Slide 18: LRU Counter Example
A
0
B
1
C
2
D
3
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
D
C
A
E
C
B
Set
Line
3
0
1
2
Line X accessed (hit)
-Set counter to max
-Decrease all others larger than X
2
0
1
3
1
0
3
2
3
0
2
1
2
3
1
0
1
2
3
0
0
1
2
3
A
E
C
D
A
E
C
D
A
E
C
B
Line Y replaced (miss)
-Find line X with 0

## Slide 19: Approximating LRU
LRU is pretty complicated (esp. for many ways)
  Access and possibly update all counters in a set on every access (not just replacement)
Need something simpler and faster
  But still close to LRU
NMRU – Not Most Recently Used
  The entire set has one MRU pointer
  Points to last-accessed line in the set
  Replacement: Randomly select a non-MRU line
    In previous example: Choose any line not with counter 3.

## Slide 20: 3) Write policy
Do we allocate cache lines on a write?
  Write-allocate
    A write miss brings block into cache
  No-write-allocate
    A write miss leaves cache as it was
Do we update memory on writes?
  Write-through
    Immediately update lower-level memory
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced

## Slide 21: Write-Back caches: Implementation
Need a Dirty bit for each line
  A dirty line has more recent data than memory
Line starts as clean (not dirty)
Line becomes dirty on first write to it
  Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
Replacing a dirty line
  Must write data back to memory (write-back)

## Slide 22: Optimizing Cache Performance
Notes: Average memory access time = hit-time + (miss-rate*miss-penalty)

## Slide 23: Cache Perf. Metrics
Miss rate
  Fraction of cache access that results in a miss
  Hit rate = 1 – miss rate
Miss per instruction
Average memory access time (AMAT)

## Slide 24: Cache perf. metrics: Implications
Latency: AMAT = hit time + miss rate * miss penalty
  Reduce hit time
  Reduce miss penalty
  Reduce miss rate
Bandwidth
  Improve cache-access bandwidth

## Slide 25: Reducing Hit Time (1)
Small & Simple Caches are faster

## Slide 26: Small & simple caches
Why?
  Critical timing path:
    Compute the memory address with tag,
    (Cache indexing) Select set based on index,
    (Tag comparison) Comparing tags to distinguish cached lines in the same set
  Direct-mapped caches: tag compare and data transmission are done at the same time (speculative data transmission)
  Lower associativity reduces power because fewer cache lines are accessed
Used in first-level cache (L1)
Advanced Optimizations

## Slide 27: Reducing Hit Time (2)
Pipelined design of caches
  Improves bandwidth, but not latency
  Essential for L1 caches at high frequency
    Even small caches have 2-3 cycle latency at N GHz
      Pentium: 1 cycle, Pentium Pro – Pentium III: 2 cycles, Pentium 4 – Core i7: 4 cycles
  Also used in many L2 caches
Way Prediction
  Speeds up set-associative caches
  Predict which of N ways has our data, fast access as direct-mapped cache
  If mispredicted, access again as set-assoc cache
Avoid address translation
  Address translation handled by TLB
  Remove TLB access from the hit path.

## Slide 28: Avoid address translation
Virtual/physical address
  Virtual memory per user/process, used for isolated address spaces
    Virtual memory mapped to physical memory or disk
    Instr. uses virtual address, need to be translated into physical address in runtime to locate actual data on physical memory
  Page table: store the mapping from virt addr. to phys. addr.
  TLB: a cache for page-table data
Key design
  Cache line address: using virtual/physical address

## Slide 29: Physically addressed cache
Which address do we use to access cache?
TLB
Virtual
Address
Cache
Data
Physical
Address
Cache
Tags
Hit?
If TLB hit, no need to
do page table lookup
from memory
Note: data cache
accessed by physical
addresses now
Cache permissions
as well
Line address: | Tag | Index
Physical
Physical

## Slide 30: PAPT Cache
Previous slide showed Physically-Addressed Physically-Tagged cache
  Sometimes called PIPT (I=Indexed)
Con: TLB lookup and cache access serialized
  Caches already take > 1 cycle

## Slide 31: Virtually Addressed Cache
Pro: latency – no need to check TLB
Con: Must flush cache on process change
  Same VA in different processes maps to different data
Con #3: Aliasing Problem
  Several virtual pages can map to same physical page!
  -> Duplicated cache lines
  Cache index and offset can only bits from page offset not from the page number (big page size can help here)
Virtual
Address
Cache
Data
Cache
Tags
Hit?
(VIVT: vitually
indexed,
virtually tagged)
TLB
On Cache
Miss
Physical
Address
To L2
Con #2: How enforce page-level permissions?
(Page is physical, while cache data is virtually indexed)
Line address: | Tag | Index
Virtual
Virtual

## Slide 32: Virtually Indexed Physically Tagged
Pro: latency – TLB parallelized
Pro: don’t need to flush $ on process swap
Con: Aliasing still limits cache indexing (can only use bits not from the VPN/PPN)
Virtual
Address
Cache
Data
Cache
Tags
Hit?
TLB
Physical Address
=
Physical Tag
Line address: | Tag | Index
Virtual
Physical

## Slide 33: Conclusion and reading lists
Cache: Textbook 2.1, 2.2, B.1, B.2, B.3
Ack: Prof. Milos’s slides