## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Cache Optimizations (3.3)
Textbook: 2.2

## Slide 2: From the last class
AMAT: average memory access time
Cache optimization techniques
  Reducing hit time
  Reducing miss penalty
  Reducing miss rate

## Slide 3: Reducing Cache Miss Rate

## Slide 4: Causes of Cache Misses
Causes of misses (3Cs)
  Compulsory
    First reference to a block
    Due to the first-time access
  Capacity
    Blocks discarded and later retrieved
    Due to limited capacity
  Conflict:
    Different memory references refer to the same cache locations (e.g. the same line in direct mapped cache)
    Due to limited associativity
Introduction

## Slide 5: Reducing miss rate (1)
“Larger cache”:
   Reduce rate of capacity misses
   Increases hit time
   Increases power consumption
“Higher associativity”:
   Reduce rate of conflict misses
   Increases hit time
   Increases power consumption
Introduction
Notes: What could affect miss rate?: capacity, associativity

## Slide 6: Reducing Cache Miss Rate (2)
Larger block size:
   Reduce compulsory misses
    Helpful if there is more spatial locality
   Increases capacity and conflict misses
   Increases miss penalty

## Slide 7: Reducing miss rates (3)
Compiler based technology
  Improve locality
  Ideal: Memory data will not be reloaded into cache.
Techniques
  Loop interchange
  Cache blocking
  Prefetch

## Slide 8: Loop Interchange
Loop interchange
    Swap nested loops to access memory in sequential order
Example:
  X[i][j] in row-major order: Last index changes first
x[i][j] and x[i+1][j] are 100 elements apart
x[i][j] and x[i][j+1] are next to each other
Notes:   Print it out!

## Slide 9: Blocking
Loop interchange works for array accessed either by row or column.
  What about matrix multiplication?
    Featuring hybrid access: sometime accessed by row and other times by column
Blocked algorithm
  Instead of accessing entire rows or columns, it subdivides matrices into blocks
  Maximize computations on block data already in cache.

## Slide 10: Example: Matrix Multiplication
  Complexity: O(N3)
  Memory references: 2N3+N2=N2 (2N+1)

## Slide 11: Matrix Multi. with Cache
Access pattern (per-matrix)
=
X
Temporal locality:
Accessed at loop 3,9,15…
0
6
12
15
9
Spatial locality:
Access by column
3

## Slide 12: Matrix Multi. with Cache
How to calculate the three elements
Per-matrix access pattern
  Is it cache friendly?
X = Y * Z

## Slide 13: Blocked Matrix Multi.
=
X
Blocked matrix multiplication
Y1
Z2
Z4
Y2
X3
X4
X1
Y1*Z2
Y2*Z4
X2

## Slide 14: Blocked M.M.: Why It Works?
Blocked matrix multiplication
Unblocked matrix multiplication
=
X
Y1*Z2
Y1
Z2
Z4
Y2
Y2*Z4
X1
=
X
Assumption
Cache capacity is 18 cells
Cache uses LRU
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 15: Blocked M.M.: Why It Works?
Blocked matrix multiplication
  X2 = Y1*Z2+Y2*Z4
Assumption
Cache capacity is 18 cells
Cache uses LRU
X = Y * Z
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 16: Blocked M.M.: Why It Works?
Matrix multiplication with no blocking
Assumption
Cache capacity is 18 cells
Cache uses LRU
X = Y * Z
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 17: Blocked M.M.: Why It Works?
No repeated memory access: 2B2
N/B
N/B
N=N/B*B
With blocking (Block size: B)
Total cache misses:
  2N3/B + N2 (=2B2*(N/B)3 + B*N/B*N)
  Without blocking: 2N3 + N2 (worst case)
Notes: Why 2B*N/B*N/B*N?
Because in loop i, N= N/B * B; when it is within step B, it will not incur any cache misses; but when out of B, it will incur new miss. The assumption here is that B is chosen such that those two “green” rectangles can fit into cache.
B*N/B*N is that x[i][j] is not changed by N2, but affected by kk or k.
B*N/B*N is write miss to output matrix
While 2N^3/B +N^2 is read-miss to two input matrix

## Slide 18: Prefetching
Start fetching block earlier
  Overlap miss latency with work before miss
Load
L1
L2
Data
Memory
Total Load-to-Use Latency
Prefetch
Data
Load
Much improved Load-to-Use Latency
Somewhat improved Latency
May cause resource
contention due to
extra cache/memory
activity

## Slide 19: Prefetching
Predict future misses and get data into cache
  If access does happen, we have a hit now (or a partial miss, if data is on the way)
  If access does not happen, cache pollution (replaced other data with junk we don’t need)
To avoid pollution, prefetch buffers
  Pollution a big problem for small caches
  Have a small separate buffer for prefetches
    When we do access it, put data in cache
    If we don’t access it, cache not polluted

## Slide 20: Software Prefetching
Two flavors: register prefetch and cache prefetch
Each flavor can be faulting or non-faulting
  Non-faulting: prefetch can’t cause exceptions if address bad
Faulting register prefetch is binding
  It is a normal load, address must be OK, uses register
Non-faulting cache prefetch is non-binding
  If address bad, becomes a NOP
  Does not affect register state
  Has more overhead (load still there), ISA change (prefetch instruction), complicates cache (prefetches and loads different)

## Slide 21: Software Prefetching
A
C
B
R1 = [R2]
R3 = R1+4
(Cache missing
instruction in red)
A
C
B
R3 = R1+4
R1 = [R2]
Hopefully the load miss
is serviced by the time
we get to the consumer
R1 = R1- 1
R1 = R1- 1
Reordering can
mess up your
code
A
C
B
R1 = [R2]
R3 = R1+4
R0 = [R2]
Using a prefetch instruction
(or load to $zero) can help
to avoid problems with
data dependencies

## Slide 22: Hardware Prefetching
Memory
CPU
HW
Prefetcher
Depending on prefetch
algorithm/miss patterns,
prefetcher injects
additional memory
requests
Cannot be overly aggressive
since prefetches may contend
for memory bandwidth, and
may pollute the cache (evict
other useful cache lines)
Fetch two blocks on miss (include next sequential block)
Hardware monitors miss traffic to memory

## Slide 23: Compiler based technology
How to optimize cache-aware memory accesses?
  How to be aware of hierarchical caches?
  How to automatically optimize access (regardless cache sizes)?
  …

## Slide 24: Summary
Advanced Optimizations

## Slide 25: Pop quiz (March 8)
What are three factors in cache performance?
How will a larger block affect the three factors (fixed sized cache)?
What are the approaches to improve program locality?

## Slide 28: Cache and address translation

## Slide 29: Avoid address translation in cache hit path
Virtual/physical address
  Virtual memory per user/process, used for isolated address spaces
    Virtual memory mapped to physical memory or disk
    Instr. uses virtual address, need to be translated into physical address in runtime to locate actual data on physical memory
  Page table: store the mapping from virt addr. to phys. addr.
  TLB: a cache for page-table data
Key design
  Cache line address: using virtual/physical address

## Slide 30: Physically addressed cache
Which address do we use to access cache?
TLB
Virtual
Address
Cache
Data
Physical
Address
Cache
Tags
Hit?
If TLB hit, no need to
do page table lookup
from memory
Note: data cache
accessed by physical
addresses now
Cache permissions
as well
Line address: | Tag | Index
Physical
Physical

## Slide 31: PAPT Cache
Previous slide showed Physically-Addressed Physically-Tagged cache
  Sometimes called PIPT (I=Indexed)
Con: TLB lookup and cache access serialized
  Caches already take > 1 cycle

## Slide 32: Virtually Addressed Cache
Pro: latency – no need to check TLB
Con: Must flush cache on process change
  Same VA in different processes maps to different data
Con #3: Aliasing Problem
  Several virtual pages can map to same physical page!
  -> Duplicated cache lines
  Cache index and offset can only bits from page offset not from the page number (big page size can help here)
Virtual
Address
Cache
Data
Cache
Tags
Hit?
(VIVT: vitually
indexed,
virtually tagged)
TLB
On Cache
Miss
Physical
Address
To L2
Con #2: How enforce page-level permissions?
(Page is physical, while cache data is virtually indexed)
Line address: | Tag | Index
Virtual
Virtual

## Slide 33: Virtually Indexed Physically Tagged
Pro: latency – TLB parallelized
Pro: don’t need to flush $ on process swap
Con: Aliasing still limits cache indexing (can only use bits not from the VPN/PPN)
Virtual
Address
Cache
Data
Cache
Tags
Hit?
TLB
Physical Address
=
Physical Tag
Line address: | Tag | Index
Virtual
Physical

## Slide 34: Conclusion and reading lists
Cache: Textbook 2.1, 2.2, B.1, B.2, B.3
Ack: Prof. Milos’s slides