## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Cache Optimizations (3.3)
Textbook: 2.2

## Slide 2: From the last class
AMAT: average memory access time
Cache optimization techniques
  Reducing hit time
  Reducing miss rate
  Reducing miss penalty

## Slide 3: Reducing Cache Miss Rate

## Slide 4: Causes of Cache Misses
Causes of misses (3Cs)
  Compulsory
    First reference to a block
    Due to the first-time access
  Capacity
    Blocks discarded and later retrieved
    Due to limited capacity
  Conflict:
    Different memory references refer to the same cache locations (e.g. the same line in direct mapped cache)
    Due to limited associativity
Introduction
Notes: Conflict cache miss -> two addresses mapped to same cache.
Check for conflict in Fully associated mapping ->( no conflict why?)

## Slide 5: Reducing miss rate (1)
“Larger cache”:
   Reduce rate of capacity misses
   Increases hit time
   Increases power consumption
“Higher associativity”:
   Reduce rate of conflict misses
   Increases hit time
   Increases power consumption
Introduction
Notes: What could affect miss rate?: capacity, associativity

## Slide 6: Reducing Cache Miss Rate (2)
Larger block size:
   Reduce compulsory misses
    Helpful if there is more spatial locality
   Increases capacity and conflict misses
   Increases miss penalty

## Slide 7: Reducing miss rates (3)
Compiler based technology
  Improve locality
  Ideal: Memory data will not be reloaded into cache.
Techniques
  Loop interchange
  Cache blocking
  Prefetch

## Slide 8: Loop Interchange
Loop interchange
    Swap nested loops to access memory in sequential order
Example:
  X[i][j] in row-major order: Last index changes first
x[i][j] and x[i+1][j] are 100 elements apart
x[i][j] and x[i][j+1] are next to each other
Notes:   Print it out!

## Slide 9: Blocking
Loop interchange works for array accessed either by row or column.
  What about matrix multiplication?
    Featuring hybrid access: sometime accessed by row and other times by column
Blocked algorithm
  Instead of accessing entire rows or columns, it subdivides matrices into blocks
  Maximize computations on block data already in cache.

## Slide 10: Example: Matrix Multiplication
  Complexity: O(N3)
  Memory references: 2N3+N2=N2 (2N+1)
Notes: 3N^2 cache misses = miss rate best
2N^3 + N^2 = cache misses worst
for(j = j + b) (N/B blocks)
{
for(k = k + b) (N/B blocks)
{
For(i++) = for(i++) to N
{ {
for (j++) for(j++; j < B)
{ {
for (k++) for(k++ ; k < B)
{ {
number of memory references = (N/B)^2* B^2 * N = O(N^3)
#ref : (N/B)^2 * N * B + 2* (N/B)^2 * N * B^2 = N^3/B + 2N^3 => we access memory for y,z matrices for B^2 , we have N/B such blocks

## Slide 11: Matrix Multi. with Cache
Access pattern (per-matrix)
=
X
Temporal locality:
Accessed at loop 3,9,15…
0
6
12
15
9
Spatial locality:
Access by column
3

## Slide 12: Matrix Multi. with Cache
How to calculate the three elements
Per-matrix access pattern
  Is it cache friendly?
X = Y * Z
Notes: Its not very cache friendly

## Slide 13: Blocked Matrix Multi.
=
X
Blocked matrix multiplication
Y1
Z2
Z4
Y2
X3
X4
X1
Y1*Z2
Y2*Z4
X2

## Slide 14: Blocked M.M.: Why It Works?
Blocked matrix multiplication
Unblocked matrix multiplication
=
X
Y1*Z2
Y1
Z2
Z4
Y2
Y2*Z4
X1
=
X
Assumption
Cache capacity is 18 cells
Cache uses LRU
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 15: Blocked M.M.: Why It Works?
Blocked matrix multiplication
  X2 = Y1*Z2+Y2*Z4
Assumption
Cache capacity is 18 cells
Cache uses LRU
X = Y * Z
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 16: Blocked M.M.: Why It Works?
Matrix multiplication with no blocking
Assumption
Cache capacity is 18 cells
Cache uses LRU
X = Y * Z
Notes: Assume cache capacity is of 18 cells
Cache is using LRU
Print it out !

## Slide 17: Blocked M.M.: Why It Works?
No repeated memory access: 2B2
N/B
N/B
N=N/B*B
With blocking (Block size: B)
Total cache misses:
  2N3/B + N2 (=2B2*(N/B)3 + B*N/B*N)
  Without blocking: 2N3 + N2 (worst case)
Notes: Why 2B*N/B*N/B*N?
Because in loop i, N= N/B * B; when it is within step B, it will not incur any cache misses; but when out of B, it will incur new miss. The assumption here is that B is chosen such that those two “green” rectangles can fit into cache.
B*N/B*N is that x[i][j] is not changed by N2, but affected by kk or k.
B*N/B*N is write miss to output matrix
While 2N^3/B +N^2 is read-miss to two input matrix

## Slide 18: Prefetching
Start fetching block earlier
  Overlap miss latency with work before miss
Load
L1
L2
Data
Memory
Total Load-to-Use Latency
Prefetch
Data
Load
Much improved Load-to-Use Latency
Somewhat improved Latency
May cause resource
contention due to
extra cache/memory
activity

## Slide 19: Prefetching
Predict future misses and get data into cache
  If access does happen, we have a hit now (or a partial miss, if data is on the way)
  If access does not happen, cache pollution (replaced other data with junk we don’t need)
To avoid pollution, prefetch buffers
  Pollution a big problem for small caches
  Have a small separate buffer for prefetches
    When we do access it, put data in cache
    If we don’t access it, cache not polluted

## Slide 20: Software Prefetching
Two flavors: register prefetch and cache prefetch
Each flavor can be faulting or non-faulting
  Non-faulting: prefetch can’t cause exceptions if address bad
Faulting register prefetch is binding
  It is a normal load, address must be OK, uses register
Non-faulting cache prefetch is non-binding
  If address bad, becomes a NOP
  Does not affect register state
  Has more overhead (load still there), ISA change (prefetch instruction), complicates cache (prefetches and loads different)

## Slide 21: Software Prefetching
A
C
B
R1 = [R2]
R3 = R1+4
(Cache missing
instruction in red)
A
C
B
R3 = R1+4
R1 = [R2]
Hopefully the load miss
is serviced by the time
we get to the consumer
R1 = R1- 1
R1 = R1- 1
Reordering can
mess up your
code
A
C
B
R1 = [R2]
R3 = R1+4
R0 = [R2]
Using a prefetch instruction
(or load to $zero) can help
to avoid problems with
data dependencies

## Slide 22: Hardware Prefetching
Memory
CPU
HW
Prefetcher
Depending on prefetch
algorithm/miss patterns,
prefetcher injects
additional memory
requests
Cannot be overly aggressive
since prefetches may contend
for memory bandwidth, and
may pollute the cache (evict
other useful cache lines)
Fetch two blocks on miss (include next sequential block)
Hardware monitors miss traffic to memory

## Slide 23: Compiler based technology
How to optimize cache-aware memory accesses?
  How to be aware of hierarchical caches?
  How to automatically optimize access (regardless cache sizes)?
  …

## Slide 24: Reducing Cache Miss Penalty

## Slide 25: Reducing Cache Miss Penalty (1)
Multilevel caches
  Very fast, small Level 1 (L1) cache
  Fast, not so small Level 2 (L2) cache
  May also have slower, large L3 cache, etc.
Why does this help?
  Miss in L1 cache can hit in L2 cache, etc.
    AMAT = HitTimeL1+MissRateL1MissPenaltyL1
    MissPenaltyL1= HitTimeL2+MissRateL2MissPenaltyL2
    MissPenaltyL2= HitTimeL3+MissRateL3MissPenaltyL3

## Slide 26: Multi-Level Caches
Memory latency = 100 cycles
16KB L1 cache, 3 cycle latency, 85% hit rate
Use two levels of caching
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  Larger 128KB cache: 6 cycle latency, 60% hit rate
One level caching: 3+0.15*100=18
Two level caching: 1+0.25*(6+0.4*100) =12.5

## Slide 27: Multi-Level Caches (2)
Global vs. Local Miss Rate
  Global L2 Miss Rate # of L2 Misses / # of All Memory Refs
  Local Miss Rate # of L2 Misses / # of L1 Misses (only L1 misses actually get to the L2 cache)
Exclusion Property
  If block is in L1 cache, it is never in L2 cache
  Saves some L2 space
Inclusion Property
  If block A is in L1 cache, it must also be in L2 cache

## Slide 28: Reducing Cache Miss Penalty (2)
Critical word first
  Why: Give requested word to loads before entire block arrive
  Request missed word from memory first
  Send it to the processor ASA it arrives
Early restart
  Why: Block transfer takes time (narrow bus)
  Request words in normal order
  Send missed word to the processor ASA it arrives
Notes: Print it out!
Both are in some way of pipelining

## Slide 29: Reducing Cache Miss Penalty (3)
Increase Load Miss Priority
  Loads can have dependent instructions
  If a load misses and a store needs to go to memory, let the load miss go first
  Need a write buffer to remember stores
Merging Write Buffer
  If multiple write misses to the same block, combine them in the write buffer
  When storing to a block that is already pending in the write buffer, update write buffer
  Use block-write instead of many small writes

## Slide 30: Non-blocking Caches
Non-blocking caches
  A blocking cache services one access at a time
    While miss serviced, other accesses blocked (wait)
  Non-blocking caches remove this limitation
    While miss serviced, can process other requests
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
Advanced Optimizations
Notes: Penalty to concurrent loads/stores

## Slide 31: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 32: Summary
Advanced Optimizations
Notes: Simple cache is direct mapped cache
Instead of broadcast to all lines in the set , send to only one line – way-predict caches
Pipelined cache access => multiple concurrent requests, to improve throughout,
Pop Quiz
Three factors in cache performance?
Hit time, miss rate, miss penalty
Larger block affect three factors (fixe sized cache)
Cache hit time (assume direct mapped cache) -> small time to lookup because smaller lines in block size
Miss penalty – time needed to transfer bloc from RAM to cache. Larger the block miss penality tend to be longer.
Approaches to improve program locality?
Cache Miss rate – three kinds – composite, complete and conflict?
Composite miss rate will be smaller for large block size – reason being large block implies more data in the cache. (assume program exhibits spatial locality)
Capacity – no effect size is fixed
Conflict – depends on structure and placement of cache.
If direct mapped cache – more conflicts . If only one line in cache always a conflict => larger the block is more likely for conflict cache miss
Loop interchange, code cache block to improve program locality.