## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Maintaining Cache Coherence (4.2)

## Slide 2: Maintaining Cache Coherence
Hardware schemes
  Shared Caches
    Trivially enforces coherence
    Not scalable (L1 cache quickly becomes a bottleneck)
  Snooping
    Needs a broadcast network (like a bus) to enforce coherence
    Each cache that has a block tracks its sharing state on its own
  Directory
    Can enforce coherence even with a point-to-point network
    A block has just one place where its full sharing state is kept

## Slide 3: Snooping by MSI

## Slide 4: Snooping
Typical for bus-based multiprocessors
  Bus serialization maintains coherence property 3
Two flavors:
  Write-update (write broadcast)
    A write to shared data is broadcast to update all copies
    All subsequent reads will return the new written value (property 2)
    All see the writes in the order of broadcasts One bus == one order seen by all (property 3)
  Write-invalidate
    Write to shared data forces invalidation of all other cached copies
    Subsequent reads miss and fetch new value (property 2)
    Writes ordered by invalidations on the bus (property 3)
Notes: Write-update: read optimized
Write-invalidate: write optimized

## Slide 5: Update vs. Invalidate
A burst of writes by a processor to one addr
  Update: each sends an update
  Invalidate: possibly only the first invalidation is sent
Writes to different words of a block
  Update: update sent for each word
  Invalidate: possibly only the first invalidation is sent
Producer-consumer communication latency
  Update: producer sends an update, consumer reads new value from its cache
  Invalidate: producer invalidates consumer’s copy, consumer’s read misses and has to request the memory block
Which is better depends on application
  But write-invalidate is simpler and implemented in most MP-capable processors today

## Slide 6: MSI: A Write-Invalidate Snoopy Protocol
State of block B in cache C can be
  Invalid: B is not cached in C
    To read or write, must make a request on the bus
  Modified: B is dirty in C
    C has the block, no other cache has the block, and C must update memory when it displaces B
    Can read or write B without going to the bus
  Shared: B is clean in C
    C has the block, other caches have the block, and C need not update memory when it displaces B
    Can read B without going to bus
    To write, must send an upgrade request to the bus

## Slide 7: MSI Snoopy Protocol
Also called “modified”

## Slide 8: MSI Example
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A
A
A: S
A: S
Read A
Write A, A’
A: M
 I
 I
A’: M
A’
Read A
Timeline
A’:S
S

## Slide 9: Cache-To-Cache Transfers: Impl.
The case of the last step (in the prev. slide)
  CPU3 has block B in M state
  CPU0 wants to read B, puts a RdReq on bus
  Latest data, A’, need to be transferred from CPU3 to CPU0
  But how?
Solution 1: abort/retry
  CPU3 cancels CPU0’s request, issues a write back
  CPU0 later retries RdReq and gets data from memory
  Too slow (two memory latencies to move data from CPU3 to CPU0)
Solution 2: intervention
  CPU3 indicates it will supply the data (“intervention” bus signal)
  Memory sees that, does not supply data, and waits for CPU3’s data
  CPU3 starts sending the data on the bus, memory is updated
  CPU0 snoops the transfer during the write-back and gets the block

## Slide 10: Cache-To-Cache Transfers: Arbitration
Intervention works if a cache has data in M state
  Nobody else has correct data, clear who responds
What if a cache has requested data in S state
  Multiple others may have the data, who should supply it?
  Solution 1: let memory supply the data
  Solution 2: whoever wins arbitration supplies the data
Notes:   Solution 3: A separate state similar to S that indicates there are maybe others who have the block in S state, but if anybody asks for the data we should supply it

## Slide 11: MSI Example
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache

## Slide 12: Conclusion and reading lists
Multiprocessing: 5.1
Cache coherency: 5.2
Ack: Prof. Milos’s slides
Copyright © 2012, Elsevier Inc. All rights reserved.

## Slide 13: MESI Protocol
New state: Exclusive
  Data is valid and clean (like in S state)
  But this is the only cached copy (like in M state)
Benefit: bandwidth reduction
  Favor writes on exclusive over shared reads.

## Slide 14: MESI: Improving Write-after-read
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A
A
A: E
Write A, A’
M
Timeline

## Slide 15: MESI: Extra Read Overhead
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A
A
A: E
Read A
S
Timeline
A: S

## Slide 16: Detecting Other Sharers
Problem
  CPU2 wants to read A, puts RdReq on bus, receives data
  How does CPU2 know if its B should be in S or E state?
Solution: “Share” bus signal
  Always 0, except when somebody pulls it to 1
    This is called “hardwired OR”
  When CPU0 snoops CPU2’s request, it pulls “Share” to 1
  CPU2 goes to S if “Share” is 1, to E if “Share” is 0

## Slide 17: MOESI: Delayed write-back
M: Modified
  I have the only copy, and it’s dirty (memory is stale)
O: Owned
  I have the most up-to-date copy, others may have copies, too, but I am responsible for supplying data and for updating memory
E: Exclusive
  I have the only copy, but it’s clean
S: Shared
  Multiple copies, all clean (memory is up-to-date)
I: Invalid
In practice,
  MOESI is used in AMD Opteron.
  MESI is used in Intel i7.

## Slide 18: MSI Example
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
A
Write A, A’
A: M
A’: M
A’
Read A
Timeline
A’:S
S
CPU0 read M state:
Change M to S on CPU3
Update memory
Memory supply data with state S to CPU0
Expensive!

## Slide 19: MOESI Example
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
A
Write A, A’
A: M
A’: M
Read A
Timeline
A’:S
O
CPU0 read M state:
Change M to O on CPU3 !NO memory update
CPU3 supplies data on state S to CPU0

## Slide 20: Summarizing MSI,MESI,MOESI
Write optimized
Read optimized
Write invalidate
Write update
MSI
MESI
MOESI

## Slide 21: Coherence Cache Miss & False Sharing

## Slide 22: Shared Memory Performance
Another “C” for cache misses
  Still have Compulsory, Capacity, Conflict
  Now have Coherence, too
What is Coherence miss?
  Scenarios:
    Write to a cache line not in M state
    Read cache line in I state
  Overhead: communication thru bus
    Load data from bus (memory/remote cache)
    Invalidation signals to remote cache lines

## Slide 23: Coherence misses: Write non-M state
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A
A
A: S
A: S
Read A
Write A, A’
A: M
 I
 I
A’: M
Timeline
Coherence miss!
CPU3 write to non-M state: Write miss
load data with state M on CPU3
Send invalidation signals on bus
  CPU0 update S to I
  CPU2 update S to I

## Slide 24: Coherence misses: Read I state
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A
A
A: S
A: S
Read A
Write A, A’
A: M
 I
 I
A’: M
A’
Read A
Timeline
A’:S
S
Coherence miss!
CPU0 read I state: Read miss
CPU3 update state M to O/S
(Write dirty data back to memory)
CPU0 read data from mem/CPU3

## Slide 25: Coherence cache misses
Two sources:
  True sharing
    Different processors access the same data
  False sharing
    Different processors access different data,
    But they happen to be in the same block

## Slide 26: Coherence miss: False sharing
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A.x1
A
A: S
A: S
Read A.x1
Write A.x2
A: M
 I
 I
A’: M
A’
Read A.x1
Timeline
A’:S
S
Coherence miss!
Coherence miss!
Coherence misses if A.x1 and A.x2 are in same cache line (A)!

## Slide 27: Coherence miss: False sharing
Main Memory
CPU0
cache
CPU1
cache
CPU2
cache
CPU3
cache
Read A.x1
A
A: S
A: S
Read A.x1
Write B.x2
B: M
Read A.x1
Timeline
Coherence misses are eliminated if A.x1 and B.x2 are in diff. cache lines (A and B)
NO Coherence miss!
NO Coherence miss!
B

## Slide 28: Performance Study: Commercial Workload
True sharing increases with # of processors.
False sharing increases
Benchmark study setup:
On four-processor shared-memory multiprocessor
Three typical workloads
  OLTP: TPC-C
  Decision-support systems: TPC-D
  Web index search
Notes: The more processors there are (meaning more CPUs/processes/etc), the more likely it results in sharing…

## Slide 29: Performance Study: Commercial Workload
True sharing decreases
False sharing increases!
Notes: True sharing misses decrease because “additional data brought in with each cache miss is accessed before the block is replaced, due to spatial locality.” the bigger a block is, the more likely that a word is brought into local CPU before being accessed (thus no miss) caused by another word accessed in the same block.
For true sharing coherence miss specifically, the increased block size will allow one processors to access more data upon each cache miss.

## Slide 30: Directory-based coherence

## Slide 31: Directory-Based Coherence
Typically in distributed shared memory
  Works for any point-to-point network, not just bus
  Decide who gets to write when without broadcasts
For every local memory block, local directory has an entry
Directory entry indicates
  Who has cached copies of the block
  In what state do they have the block

## Slide 32: Basic Directory Scheme
Each entry for a local mem block
  One dirty bit (1 if there is a dirty cached copy)
  A presence vector of #CPU bits
    Each element bit is for one CPU node, tells wether it has a cached copy
All misses sent to block’s home
  Known by mem address (in DSM)
Directory performs needed coherence actions
Eventually, directory responds with data

## Slide 33: Read Miss
Processor CPUk has a read miss on block B, sends request to home node of the block
Directory controller
  Finds entry for B, checks D bit
  If D=0
    Read memory and send data back, set P[k]
  If D=1
    Request block from processor whose P bit is 1
    When block arrives, update memory, clear D bit, send block to Pk and set P[k]

## Slide 34: Distributed MSI Example
CPU0
cache
Dist.Memory0
CPU1
cache
CPU2
cache
CPU3
cache
Dist.Memory1
Dist.Memory2
Dist.Memory3
Interconnection Network
X
dir
Mem
Read X
Read X
X: S
X: S
X
0
1
1
Write X
 I
 I
1
0
0
0
1
X: M

## Slide 35: Directory Operation
Network controller connected to each bus
  A proxy for remote caches and memories
    Requests for remote addresses forwarded to home, responses from home placed on the bus
    Requests from home placed on the bus, cache responses sent back to home node
Each cache still has its own coherence state
  Directory is there just to avoid broadcasts and order accesses to each location
    Simplest scheme: If access A1 to block B still not fully processed by directory when A2 arrives, A2 waits in a queue until A1 is done

## Slide 36: Distributed MSI Example
CPU0
cache
Dist.Memory0
CPU1
cache
CPU2
cache
CPU3
cache
Dist.Memory1
Dist.Memory2
Dist.Memory3
Interconnection Network
X
dir
mem

## Slide 37: Conclusion and reading lists
MSI(continued): 5.2
Performance in SMP: 5.3
Directory-based coherence: 5.4
Ack: Prof. Milos’s slides
Copyright © 2012, Elsevier Inc. All rights reserved.