## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Synchronization (4.3)
Textbook: 5.5

## Slide 2: Overview
Synchronization primitive: mutex/lock
Primitive implementation: spinlock
Atomic instructions: LD/ST, RMW
Cache coherence: MSI

## Slide 3: Lock/Mutex
Program
  Lock.acquire/release
  Critical section
Execution
  Safety: no more than 1 threads run in critical sec.
  Liveness: 1 thread run in critical sec.

## Slide 4: Spinlock impl. by atomic LD/ST
Program
Execution
Notes: Program: spinlock.acq { while(splock.val == 1); splock.val = 1 } A: LD R1, V CMPL R1,1 TE A ST(set) V, 1
Rel { splock.val = 0; } R : ST v, 0

## Slide 5: Spinlock impl. by atomic RMW
Spinlock by EXCH
  Program
  Execution
Notes: acq() { while(exchange(1,val) == 1); } Mov R1,1 A: EXCH R1, val CMPL R1,1 JE A
Rel() { val = 0; }

## Slide 6: Atomic RMW instructions
swap: mov R2, R1
ll R3,x
sc x, R2
cmpl R2,0
beqz swap
mov R1,R3
Atomic Exchange
EXCH R1, x
upd: ll R2,0(R1)
add R3,R2,R4
sc R3,0(R1)
beqz R3,upd
Atomic Add to Shared Variable
t&s: mov R1,1
ll R2,x
sc R1,x
cmpl R2, 0
jne t&s
cmpl R1, 0
je t&s
Atomic Test&Set
T&S x
Swap R1 w/ x
Test if x is zero, set to one
Notes: Beqz R2, label: if R2 == zero, then jump to label
Notice atomic exchange is blocking, atomic test&set is blocking
Ll -> linkload instruction
Sc-> storeConditional (regular store instruction + some condition check)

## Slide 7: LL & SC Instructions
Atomic instructions OK, but hard to implement in HW
  Has to enforce no other operations allowed btwn memory read/write
  No other operations from all other processors
LL&SC: easier to implement in HW
  Idea: LL&SC is a pair of linked instructions
A load-linked (LL) instruction
  Like a normal load, but also remembers the address in a special-purpose “link” register (hidden in microarchitecture)
Link register is cleared if:
  Other processors’ write address matches link address
  Context switches
A store-conditional (SC) instruction
  Like a normal store, but fails if its address is not the same as that in the link register
  Returns 1 if successful, 0 on failure

## Slide 8: Backup slides

## Slide 9: The Concept of Synchronization

## Slide 10: Synchronization
In multi-processing, it may need to synchronize the program execution on different processors.
Use Cases:
Bank account transfer problem.
  Alice transfer $1000 to Bob
      Alice.balance -= 1000;
      Bob.balance += 1000;
Shared counter, sum updates, etc…

## Slide 11: Locking/Mutual Exclusion
Lock/mutex
  Acquire the lock
  Critical section
  Release the lock
The lock variable is used for mutual exclusion
  Only one processor can own the lock
    Many processors may call lock(), but only one will succeed (others block)
    The winner runs the critical section code, then release the lock
    Now one of the others gets it, etc.
Lock_acq();
Alice.balance -= 1000;
Bob.balance += 1000;
Lock_release();

## Slide 12: Implementing the lock
Use a shared variable (1 – owned, 0 –free)
Releasing a lock is easy
  Just set it to 0
Acquiring a lock, how?
  Spin waiting for shared variable to become 0
Lock_release(){
mutex_var = 0;
}
Lock_acq(){
while(mutex_var== 1);
mutex_var == 1
}
But when mutex_var becomes 0, it will be seen by all processors.
Need a way to atomically see that the mutex is 0 and set it to 1

## Slide 13: Hardware Primitive: Atomic Instructions

## Slide 14: Locks by atomic exchange
Atomic exchange
  Swaps register with memory location
  E.g., EXCH R1,78(R2) will swap content of register R1 and mem location at address 78+R2
  (Read and write operations indivisible in one instruction)
Notes: Forget about cache!

## Slide 15: Locks by atomic exchange
To acquire a mutex, 1 in R1 and EXCH
  Then look at R1 and see whether mutex acquired
  If R1 is 1, mutex was owned by somebody else and we will need to try again later
  If R1 is 0, mutex was free and we set it to 1, which means we have acquired the mutex
Lock_acq(){
movq R1, 1
Lck: exch R1,0(R2)
bnez R1,lck
}
Notes: Forget about cache!

## Slide 16: Other Hardware Primitives: Atomic Read-Update Instructions
Test-and-set
  Test and set a variable until it passes the test.
Fetch-and-increment
  Reads original value from memory and increments it in memory: e.g. mem:v  mem:v+1, register:v
Requires memory read and write in uninterruptable instruction

## Slide 17: LL & SC Instructions
Atomic instructions OK, but hard to implement in HW
  Has to enforce no other operations allowed btwn memory read/write
  No other operations from all other processors
LL&SC: easier to implement in HW
  Idea: LL&SC is a pair of linked instructions
A load-linked (LL) instruction
  Like a normal load, but also remembers the address in a special-purpose “link” register (hidden in microarchitecture)
Link register is cleared if:
  Other processors’ write address matches link address
  Context switches
A store-conditional (SC) instruction
  Like a normal store, but fails if its address is not the same as that in the link register
  Returns 1 if successful, 0 on failure

## Slide 18: Using LL & SC
swap: mov R2, R1
ll R3,x
sc x, R2
cmpl R2,0
beqz swap
mov R1,R3
Atomic Exchange
EXCH R1, x
upd: ll R2,0(R1)
add R3,R2,R4
sc R3,0(R1)
beqz R3,upd
Atomic Add to Shared Variable
t&s: mov R1,1
ll R2,x
sc R1,x
bnez R2,t&s
beqz R1,t&s
Atomic Test&Set
T&S x
Swap R1 w/ x
Test if x is zero, set to one
Notes: Beqz R2, label: if R2 == zero, then jump to label
Notice atomic exchange is blocking, atomic test&set is blocking

## Slide 19: Using LL & SC
swap: mov R2, R1
ll R3,x
sc x, R2
cmpl R2,0
beqz swap
mov R1,R3
Atomic Exchange
EXCH R1, x
upd: ll R2,0(R1)
add R3,R2,R4
sc R3,0(R1)
beqz R3,upd
Atomic Add to Shared Variable
t&s: mov R1,1
ll R2,x
sc R1,x
cmpl R2, 0
jne t&s
cmpl R1, 0
je t&s
Atomic Test&Set
T&S x
Swap R1 w/ x
Test if x is zero, set to one
Notes: Beqz R2, label: if R2 == zero, then jump to label
Notice atomic exchange is blocking, atomic test&set is blocking

## Slide 20: Performance: Lock Using Coherence

## Slide 21: Implementing locks: Efficiency
Spinning by one atomic instruction works w.o. cache
But is very inefficient if there’s cache coherence
  Think about a process getting stuck at acquiring the lock
  Exch is swapping 1 with 1: redundant memory writes
  More-over, a lot of invalidations!
    Every write sends an invalidation for cache coherence.
Lock_acq(){
movq R1, 1
Lck: exch R1,0(R2)
bnez R1,lck
}

## Slide 22: Implementing locks: Efficiency
More efficient: first do reads on a local copy
  Read, do swap only if 0
    Read of 0 does not guarantee success (not atomic)
    But if 1 we have little chance of success
  Write only when good chance we will succeed
  When it spins, always spins on LD, which is efficient
Lock_acq(){
Lck: ld R1,0(R2) ;regular LD on cached copy
bnez R1,lck ;more likely to get the lock
mov R1,1
exch R1,0(R2) ;invoked less frequently
bnez R1,lck
}

## Slide 23: Example: Test and Set
try: mov R3,#1
ll R2,0(R1)
sc R3,0(R1)
bnez R2,try
beqz R3,try
CPU1
CPU2
Shared memory
mov R3,#1
ll R2,0(R1)
sc R3,0(R1)
bnez R2,try
beqz R3,try
mov R3,#1
ll R2,0(R1)
sc R3,0(R1)
bnez R2,try
mov R3,#1
ll R2,0(R1)
…
It spins on sc
Sc is expensive!
  Write invalidation
Sc swaps 1 and 1!

## Slide 24: Example: Test and Test and Set
try: mov R3,#1
ll R2,0(R1)
sc R3,0(R1)
bnez R2,try
beqz R3,try
try: mov R3,#1
ll R2,0(R1)
bnez R2,try
sc R3,0(R1)
beqz R3,try
CPU1
CPU2
Shared memory
mov R3,#1
ll R2,0(R1)
bnez R2,try
sc R3,0(R1)
beqz R3,try
mov R3,#1
ll R2,0(R1)
bnez R2,try
mov R3,#1
ll R2,0(R1) …

## Slide 25: Large-Scale Systems: Locks
Contention even with test-and-test-and-set
  Every write goes to many, many spinning procs
  Making everybody test less often reduces contention for high-contention locks but hurts for low-contention locks
  Solution: exponential back-off
    If we have waited for a long time, lock is probably high-contention
    Every time we check and fail, double the time between checks
      Fast low-contention locks (checks frequent at first)
      Scalable high-contention locks (checks infrequent in long waits)
  Special hardware support