## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Synchronization & Consistency (4.4)

## Slide 2: Uniprocess lock
Interrupt disabling lock
  Acq() { disable_interrupt(); }
  Rel() { enable_interrupt(); }
Execution
Thread state

## Slide 3: Queue lock
Key idea: when waiting for the lock, wait in scheduler as well.
Program
Execution
  Acq(){
  if(lock.val==busy)
  lock.waiting.add(this);
  this_thread_sleep&switch();
  }
  Acq(){
  if(lock.waiting.isNotEmpty()){
  next=lock.waiting.remove();
  next.resume();
  } else lock.val=free;

## Slide 4: Queue lock versus Spin lock
Spinlock: thread in waiting the lock is runnable in scheduler.
Queue lock: thread when waiting the lock is waiting in the scheduler.
Notes: Scheduler will not schedule Queue lock because it is already sleeping in the scheduler. In linux systems we implement Queue lock.

## Slide 5: Barrier

## Slide 6: Barrier Synchronization
All must arrive before any can leave
  Used between different parallel sections
Uses two shared variables
  A counter that counts how many have arrived
  A flag that is set when the last processor arrives
Notes: lock versus barrier
- lock: first arrive first serve
- barrier: all can be served once all arrive
- Lock: one shared variable
- Barrier: two shared variable

## Slide 7: Simple Barrier Synchronization
lock(counterlock);
if(count==0) release=0; /* First resets release */
count++; /* Count arrivals */
unlock(counterlock);
if(count==total){ /* All arrived */
count=0; /* Reset counter */
release = 1; /* Release processes */
}else { /* Wait for more to come */
spin(release==1); /* Wait for release to be 1 */
}
Problem: not really reusable when multiple barriers.

## Slide 8: Executing simple barrier synchronization
lock(counterlock);
if(count==0) release=0;
count++;
unlock(counterlock);
if(count==total){
count=0;
release = 1;
}else {
spin(release==1);
}
// doing some other work
lock(counterlock);
if(count==0) release=0;
count++;
unlock(counterlock);
if(count==total){
count=0;
release = 1;
}else {
spin(release==1);
}
Process Fast
Process Slow
lock(counterlock);
if(count==0) release=0;
count++;
unlock(counterlock);
//preempted: start
//preempted: end
if(count==total){
count=0;
release = 1;
}else {
spin(release==1);
}
Time line
0
1
Release
Counter
0
1
1
0
0
1
0
1
Release
Counter
Spinning
Spinning
Deadlock
Notes: Example:
  Two processes: fast and slow
  Slow arrives first, reads release, sees 0
  Fast arrives, sets release to 1, goes on to execute other code, comes to barrier again, resets release, starts spinning
  Slow now reads release again, sees 0 again
  Now both processors are stuck and will never leave

## Slide 9: Correct Barrier Synchronization
localSense=!localSense; /* Toggle local sense */
lock(counterlock);
count++; /* Count arrivals */
if(count==total){ /* All arrived */
count=0; /* Reset counter */
release=localSense; /* Release processes */
}
unlock(counterlock);
spin(release==localSense); /* Wait to be released */
Release in first barrier acts as reset for second
  When fast comes back it does not change release, it just waits for it to become 0
  Slow eventually sees release is 1, stops spinning, does work, comes back, sets release to 0, and both go forward.
Local to processor

## Slide 10: Executing correct barrier synchronization
localSense=!localSense;
lock(counterlock);
count++
if(count==total){
count=0;
release=localSense;
}
unlock(counterlock);
spin(release==localSense);
// doing some other work
localSense=!localSense;
lock(counterlock);
count++
if(count==total){
count=0;
release=localSense;
}
unlock(counterlock);
spin(release==localSense);
Process Fast
Process Slow
localSense=!localSense;
lock(counterlock);
count++
if(count==total){
count=0;
release=localSense;
}
unlock(counterlock);
//preempted: start
//preempted: end
spin(release==localSense);
Time line
0
1
Release
Counter
0
1
1
0
1
0
1
1
Release
Counter
1
Local sense
0
Local sense
1
1
1
init: localSense = 0,
release = 0
localSense is local to process!
Spinning
Proceed!
Proceed!

## Slide 11: Executing correct barrier synchronization (2)
spin(release==localSense);
Process Fast
Process Slow
spin(release==localSense);
// do some other work
localSense=!localSense;
lock(counterlock);
count++
if(count==total){
count=0;
release=localSense;
}
unlock(counterlock);
spin(release==localSense);
Time line
1
0
1
1
1
1
Spinning
Proceed!
0
0
0
Release
Counter
Local sense
0
0
0
Proceed!
Proceed!

## Slide 12: Large-Scale Systems: Barriers
Barrier with many processors
  Have to update counter one by one – takes a long time
  Solution: use a combining tree of barriers
    Example: using a binary tree
    Pair up processors, each pair has its own barrier
      E.g. at level 1 processors 0 and 1 synchronize on one barrier, processors 2 and 3 on another, etc.
    At next level, pair up pairs
      Processors 0 and 2 increment a count a level 2, processors 1 and 3 just wait for it to be released
      At level 3, 0 and 4 increment counter, while 1, 2, 3, 5, 6, and 7 just spin until this level 3 barrier is released
      At the highest level all processes will spin and a few “representatives” will be counted.
    Works well because each level fast and few levels
      Only 2 increments per level, log2(numProc) levels
      For large numProc, 2*log2(numProc) still reasonably small

## Slide 13: Large-Scale Systems: Locks
Contention even with test-and-test-and-set
  Every write goes to many, many spinning procs
  Making everybody test less often reduces contention for high-contention locks but hurts for low-contention locks
  Solution: exponential back-off
    If we have waited for a long time, lock is probably high-contention
    Every time we check and fail, double the time between checks
      Fast low-contention locks (checks frequent at first)
      Scalable high-contention locks (checks infrequent in long waits)
  Special hardware support

## Slide 14: Memory Consistency

## Slide 15: Memory Consistency: Program order
Coherence is about order of accesses to the same address
Consistency is about order of accesses to different addrs
Possible outcomes on Proc 2 in program order
  (F,D) can be (0,0), (0,1), (1,1)
  (F,D) can’t be (1,0)!
Proc 1
ST 1->D
ST 1->F
Proc 2
LD F
LD D
Program order
ST D
ST F
LD F
LD D
(1,1)
LD F
ST D
LD D
ST F
(0,1)
(0,0)
LD F
LD D
ST D
ST F
*
ST F
LD F
*
(1,*)
ST D
ST F
LD F
LD D
(1,1)

## Slide 16: Memory Consistency: Execution (re)order
Possible outcomes on Proc 2 in program order
  (F,D) can be (0,0), (0,1), (1,1)
  (F,D) can’t be (1,0)!
Execution (re)ordering can give (1,0)
  Exposes instruction reordering to programmer
  We need something that makes sense intuitively
Proc 1
ST 1->D
ST 1->F
Proc 2
LD F
LD D
Program order
Execution order
Proc 1
ST D
ST F
Proc 2
LD D
LD F
Proc 2 can reorder loads
(1,0)
LD D
ST D
ST F
LD F

## Slide 17: Reordered LD/ST is real!
Realistic example: flag synchronization
  Producer produces data and sets flag
  Consumer waits for flag to be 1, then reads data
Now we can have the following situation
  Proc 2 has cache miss on F, predicts the branch NT, reads D
  Proc 1 writes D, writes F
  Proc 2 gets F, checks, sees 1 => branch is correctly predicted
Proc 1
D=Val1;
F=1;
Proc 2
while(F==0);
Val2=D;
Source Code
Proc 1
ST D
ST F
Proc 2
wait: LD F <1>
BEQZ F,wait <2>
LD D <3>
Assembler Code
Notes: ------------------------------------time line-------------------------------
<1> ---------cache miss-----------+-------+--mem read-- <1>
<2>------------------------------+-------+------------------------ <2>
<3>--cache hit-> <3> | |
| |
| |
problem in between!

## Slide 18: Sequential Consistency
Consistency is about ordering between operations;
  Operation X must complete before operation Y is done.
  Ordering should be the same when different processors are arbitrarily interleaved
  The order seen by everyone.
Sequential consistency requires:
  R → W, R → R, W → R, W → W
Simple implementation
  A processor issues next access only when all previous accesses (from it or other processors) are complete
  Sloooow!
A better implementation
  Processor issues accesses as it sees fit, but detects and fixes potential violations of sequential consistency

## Slide 19: Relaxed Consistency Models
Relax W → R
  “Total store ordering”
Relax W → W
  “Partial store order”
Relax R → W and R → R
  “Weak ordering” and “release consistency”

## Slide 20: Relaxed Consistency Models
Two kinds of memory accesses
  Data accesses and synchronization accesses
Synchronization accesses determine order
  Data accesses ordered by synchronization
  Any two of accesses to the same variable in two different processes, such that at least one of the accesses is a write, are always ordered by synchronization operations
Good performance even in simple implementation
  Sequential consistency for sync accesses
  Data accesses can be freely reordered (except around sync accesses)

## Slide 21: Relaxed Consistency Models
Data Races
  When data accesses to same variable in different processors are not ordered by sync
  Most programs are data-race-free (so relaxed consistency models work well)
There are many relaxed models
  Weak Consistency, Processor Consistency, Release Consistency, Lazy Release Consistency, Scope
  All work just fine for data-race-free programs
  But when there are data races, more relaxed models  weirder program behavior

## Slide 22: Example: Release Consistency
Defines two types of sync operations
  Acquire (intend to read shared data)
    E.g. mutex_lock(), cond_wait()
  Release (done writing shared data)
    E.g. mutex_unlock(), cond_signal()
Any ordering of accesses is possible, except
  Acquire and release not reordered
  Reads not reordered with acquire before them
  Writes not reordered with release after them

## Slide 23: Locks in Release Consistency
This works just fine:
mutex_lock(L);
x=x+1;
y=y+1;
mutex_unlock(L);
mutex_lock(L);
x=x-1;
y=y-1;
mutex_unlock(L);
LD R1, x
ADD R1, $1, R1
ST x, R1
Have both LD and ST, can’t be scheduled either before lock() or after unlock()
Notes: //regarding x, this compile to both LD and ST

## Slide 24: Release Consistency Problems
This does not work as expected:
mutex_lock(L);
a=x;
b=y;
mutex_unlock(L);
mutex_lock(L);
x=1;
y=1;
mutex_unlock(L);
MOV R1, $1
ST x, R1
Has only ST
Can be scheduled before lock()
May mixed with a=x

## Slide 25: Conclusion and reading lists
Synchronization: 5.5
Memory consistency: 5.6
Ack: Prof. Milos’s slides
Copyright © 2012, Elsevier Inc. All rights reserved.

## Slide 26: Pop Quiz - 3
In MSI, how many bits are needed to keep state (per memory block)?
What’s the benefit of having multi-level page table (versus one-level page table)?
  Reducing memory access latency
  Reducing the page-table size
  Increasing memory access throughput
  Reducing cache miss rate
[True/False] Page fault occurs before address translation.