## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Storage (5.1)

## Slide 2: Storage Systems
I/O performance (bandwidth, latency)
  Bandwidth improving, but not as fast as CPU
  Latency improving very slowly
  Consequently, by Amdahl’s Law: fraction of time spent on I/O increasing
Other factors just as important
  Reliability, Availability, Dependability
Storage devices very diverse
  Magnetic disks, tapes, CDs, DVDs, flash
  Different advantages/disadvantages and uses

## Slide 3: Storage Devices

## Slide 4: Magnetic Disks

## Slide 5: Magnetic Disks
Good: cheap ($/MB), fairly reliable
  Primary storage, memory swapping
Bad: Can only read/write an entire sector
  Can not be directly addressed as main memory
Disk access time
  Queuing delay
    Wait until disk gets to do this operation
  Seek time
    Head moves to correct track
  Rotational latency
    Correct sector must get under the head
  Data transfer time and controller time

## Slide 6: Trends for Magnetic Disks
Capacity: doubles in approx. one year
Average seek time
  5-12ms, very slow improvement
Average rotational latency (1/2 full rotation)
  5,000 RPM to 10,000 RPM to 15,000 RPM
  Improves slowly, not easy (reliability, noise)
Data transfer rate
  Improves at an OK rate
    New interfaces, more data per track

## Slide 7: Optical Disks
Improvement limited by standards
  CD and DVD capacity fixed over years
  Technology actually improves, but it takes time for it to make it into new standards
Physically small, Replaceable
  Good for backups and carrying around

## Slide 8: Magnetic Tapes
Very long access latency
  Must rewind tape to correct place for read/write
Very cheap
  It’s just miles of tape!
Used for backup (secondary storage)
  Large capacity & Replaceable
  Performance tolerable for linear/sequential access (e.g., writing backups)
Dying out
  Low volume, so cost decreases slower than disks
  Cheaper to use disks now

## Slide 9: Using RAM for Storage
Disks are about 100 times cheaper ($/MB)
DRAM is about 100,000 faster (latency)
Solid-State Disks
  Was a DRAM and a battery
    Much faster than disk, more reliable
    Expensive (not very good for archives and such)
  Now: Flash memory
    Much faster than disks, but slower than DRAM
    Very low power consumption
    Smaller capacity than disks (GB vs. TB)
    Can only write 1,000,000 many times

## Slide 10: Hybrid Magnetic-Flash
Magnetic is cheap, huge capacity
  Power-hungry (always spinning)
  Slow (must move heads)
  Need large buffer to improve access scheduling
  Sensitive to impact while spinning
Flash is fast but small capacity
  Fast, power-efficient, no moving parts
Idea: have both
  Buffer writes on flash (use flash as cache for writes)
  Can spin down magnetic drive, spin up occasionally to write “dirty” blocks

## Slide 11: Storage IO

## Slide 12: Buses for I/O
Traditionally, two kinds of busses
  CPU-Memory bus (fast, short)
  I/O bus (can be slower and longer)
Now: mezzanine buses (PCI)
  Pretty fast and relatively short
  Can connect fast devices directly
  Can connect to longer, slower I/O busses
Data transfers over a bus: transactions
Notes: Mezzanine: me-zer-nin

## Slide 13: Buses in a System
Notes: Pci express

## Slide 14: How does read() works?

## Slide 15: Bus Design Decisions
Split transactions
  Traditionally, bus stays occupied between request and response on a read
  Now, get bus, send request, free bus (when response ready, get bus, send response, free bus)
Bus mastering
  Which devices can initiate transfers on the bus
  CPU can always be the master
  But we can also allow other devices to be masters
  With multiple masters, need arbitration

## Slide 16: Interface to access IO devices
Application-level IO:
  What is usually written in your program
  Provided by language runtime (e.g. libc)
  Example: Standard I/O (stdio.h) by C
    Printf, scanf, fopen …
System-level IO:
  Directly by system calls
  Example: POSIX syscalls: open, close, read/write, state
  Allow you to access raw data on disk (e.g. inode)
CPU-device IO:
  Device driver’s view
App
Libc
OS
Device driver
IO Device
Memory

## Slide 17: CPU-Device Interface (Device driver’s view)
Devices accessible to CPU thru device registers (data/control)
These registers can be either
  Memory mapped IO
    Some physical memory addresses map to I/O device registers (inside the IO device)
    Read/write through LS/ST
    Most RISC processors support only this kind of I/O mapping
  Port mapped IO:
    In a separate I/O address space: dedicated IO pin or bus
    Read/write through special IN/OUT instrs
    Used in x86, but even in x86 PCs some I/O is memory mapped
CPU
Physical Memory
Disk
NI
Phy. memory address space
Notes: http://en.wikipedia.org/wiki/Memory-mapped_I/O
IO device register represents IO device!

## Slide 18: CPU-Device Interface
Devices can be very slow
  When given some data, a device may take a long time to become ready to receive the data
  Usually we have a Done bit in status register
Checking the Done bit
  Polling: test the Done bit in a loop
  Interrupt: interrupt CPU when Done bit becomes 1
  Interrupts if I/O events infrequent or if device is slow
    Each interrupt has some OS and HW overhead
  Polling better for devices that are done quickly
    Even then, buffering data in the device lets us use interrupts
  Interrupt-driven I/O used today in most systems
CPU
Physical Memory
Disk
NI
Phy. memory address space

## Slide 19: IO Performance

## Slide 20: IO performance
Metrics
  Throughput, or bandwidth in context of IO
  Response time, or latency in context of IO
Trade-off btwn throughput and response time
  Improving throughput favors non-empty queue
  Improving latency favors empty queue

## Slide 21: Throughput versus response time

## Slide 22: SPEC File Server Benchmarks
x
With 168 15k RPM 72GB disks

## Slide 23: Dependability

## Slide 24: Recap: Reliability and Availability
System can be in one of two states
  Service Accomplishment
  Service Interruption
Reliability
  Measure of continuous service accomplishment
  Typically, Mean Time To Failure (MTTF)
Availability
  Service accomplishment as a fraction of overall time
  Also looks at Mean Time To Repair (MTTR)
    MTTR is the average duration of service interruption
  Availability=MTTF/(MTTF+MTTR)
Failure
Restorations
Time-line
MTTR
MTTF
MTBF

## Slide 25: Dependability
Quality of delivered service that justifies us relying on the system to provide that service
  Delivered service is the actual behavior
  Each module has an ideal specified behavior
Faults, Errors, Failures
  Failure: actual deviates from specified behavior
  Error: defect that results in failure
  Fault: cause of error
Notes: Reliability : external metrics
depende

## Slide 26: Failure Example
A programming mistake is a fault
  An add function that works fine, except when we try 5+3, in which case it returns 7 instead of 8
  It is a latent error until activated
An activated fault becomes effective error
  We call our add and it returns 7 for 5+3
Failure when error results in deviation in behavior
  E.g. we schedule a meeting for the 7th instead of 8th
  An effective error need not result in a failure (if we never use the result of this add, no failure)
Notes: Latent error: hidden error

## Slide 27: Faults Classified by Cause
Hardware Faults
  Hardware devices fail to perform as designed
Design Faults
  Faults in software and some faults in HW
  E.g. the Pentium FDIV bug was a design fault
Operation Faults
  Operator and user mistakes
Environmental Faults
  Fire, power failure, sabotage, etc.
Notes: Pentium FDIV bug is one of the most infamous bugs by Intel. It is a bug in Intel Pentium FPU; for some calculation, it can not produce correct result beyond 4 digits.

## Slide 28: Faults Classified by Duration
Transient Faults
  Last for a limited time and are not recurring
  An alpha particle can flip a bit in memory but usually does not damage the memory HW
Intermittent Faults
  Last for a limited time but are recurring
  E.g. overclocked system works fine for a while, but then crashes… then we reboot it and it does it again
Permanent Faults
  Do not get corrected when time passes
  E.g. the processor has a large round hole in it because we wanted to see what’s inside…
Notes: Alpha particle is a radiation particle that may change the status of memory bits.

## Slide 29: Improving Reliability
Fault Avoidance:
  Prevent occurrence of faults by better HW construction
Fault Tolerance
  Prevent faults from becoming failures
  Typically done through redundancy
Error Removal
  Removing latent errors by verification
Error Forecasting
  Estimate presence, creation, and consequences of errors