## Slide 1: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
RAID (5.2)

## Slide 2: Recap: Reliability and Availability
System can be in one of two states
  Service Accomplishment
  Service Interruption
Reliability
  Measure of continuous service accomplishment
  Typically, Mean Time To Failure (MTTF)
Availability
  Service accomplishment as a fraction of overall time
  Also looks at Mean Time To Repair (MTTR)
    MTTR is the average duration of service interruption
  Availability=MTTF/(MTTF+MTTR)
Failure
Restorations
Time-line
MTTR
MTTF
MTBF

## Slide 3: Redundant Array of Inexpensive Disks

## Slide 4: Disk Fault Tolerance with RAID
Redundant Array of Inexpensive Disks
  Several smaller disks play a role of one big disk
Can improve performance
  Data spread among multiple disks
  Accesses to different disks go in parallel
Can improve reliability
  Data can be kept with some redundancy
And reliability is a more important issue in RAID than in one disk…
  Inexpensive

## Slide 5: RAID 0
Data striping used to improve performance
  Data striping is about partitioning logically sequential data, such as a file, so that consecutive “stripes” are stored on different physical storage devices.
  Disk load balanced, which improves
    Throughput: all disks can work in parallel
    Latency: less queuing delay – a queue for each disk
No Redundancy
  Reliability is actually lower than a single disk (if any disk in array fails, we have a problem)

## Slide 6: RAID 0 Reliability
P - probability that a drive will die during one hour
  For a single drive, MTTF = 1/P hours
For RAID 0 with two drives:
  Probability that both drives survive an hour: (1-P) (1-P)
  Probability of failure: 1-(1-P)2
  MTTF is 1/(1-(1-P)2)
Say P=0.01, MTTF is
  100 hours for single drive
  50.25 hours for 2-drive RAID-0
  25.38 hours for 4-drive RAID-0
Notes: Pr[A AND B]=Pr[A]*Pr[B]=(1-P)(1-P)
P[^A OR ^B]=1-Pr[A AND B]=1-(1-P)^2

## Slide 7: RAID 1
Disk mirroring [replication]
  Disks paired up, keep identical data
  A write must update copies on both disks
  A read can read any of the two copies
Improved performance and reliability
  Can do more reads per unit time
  If one disk fails, its mirror still has the data
If we have more than 2 disks (e.g. 8 disks)
  “Striped mirrors” (RAID 1+0)
    Pair disks for mirroring, striping across the 4 pairs
  “Mirrored stripes” (RAID 0+1)
    Do striping using 4 disks, then mirror that using the other 4

## Slide 8: RAID 1 Reliability
P - probability that a drive will die during one hour
  For a single drive, MTTF = 1/P hours
For RAID 1 with two drives:
  Probability that both drives fail during one hour: P2
  MTTF is 1/P2
Say P=0.01, MTTF is
  100 hours for single drive
  10,000 hours for 2-drive RAID-1
  100,000,000 hours for 4-drive RAID-0
Notes: P[^A AND ^B]=Pr[^A]*Pr[*B]=P^2

## Slide 9: RAID 2/3/4
Idea of error-correcting code (ECC)
  Example: parity by XOR
    1,0,0,1, s
    s=1 XOR 0 XOR 0 XOR 1
RAID 2: memory style ECC
RAID 3: bit-interleaved parity
RAID 4: Block-interleaved parity

## Slide 10: RAID 4
Block-interleaved parity
  One disk is a parity disk, keeps parity blocks
  Parity block at position X is the parity for all blocks whose position is X on any of the data disks
  A read accesses only the data disk where the data is
  A write must update the data block and its parity block
  Can recover from an error on any one disk
    Use parity and other data disks to restore lost data
  Note that with N disks we have N-1 data disks and only one parity disk, but can still recover when one disk fails
  But write performance worse than with one disk (all writes must read and then write the parity disk)

## Slide 11: RAID 4 Parity Update

## Slide 12: RAID 5
Distributed block-interleaved parity
  Like RAID 4, but parity blocks distributed to all disks
  Read accesses only the data disk where the data is
  A write must update the data block and its parity block
    But now all disks share the parity update load
Notes: The write to parity disk drive is not evenly distirbuted. No load balancing.
In RAID5 there is distribution of parity bits among all five drives.

## Slide 13: RAID 5 Reliability
P - probability that a drive will die during one hour
  For a single drive, MTTF = 1/P hours
For RAID 5 (and RAID 4) with 4 drives:
  Probability that none of the four drives fails: (1-P)4
  Probability that exactly one drive fails: 4*P* (1-P)3
  Probability that 2 or more drives fail:
  1- [(1-P)4+4*P* (1-P)3]
Say P=0.01, MTTF is
  100 hours for single drive
  10,000 hours for 2-drive RAID-5 (same as RAID-1)
  1,689 hours for 4-drive RAID-5

## Slide 14: RAID 6
Two different (P and Q) check blocks
  Each protection group has
    N-2 data blocks
    One parity block
    Another check block (not the same as parity)
Can recover when two disks are lost
  Think of P as the sum and Q as the product of D blocks
  If two blocks are missing, solve equations to get both back
More space overhead (only N-2 of N are data)
More write overhead (must update both P and Q)
  P and Q still distributed like in RAID 5

## Slide 15: Dependability

## Slide 16: Dependability: from Failure to Fault
Quality of delivered service that justifies us relying on the system to provide that service
  Delivered service is the actual behavior
  Each module has an ideal specified behavior
Faults, Errors, Failures
  Failure: actual deviates from specified behavior (effect)
  Error: defect that results in failure
  Fault: cause of error
Notes: Reliability : external metrics
depende

## Slide 17: Failure Example
A programming mistake is a fault
  An add function that works fine, except when we try 5+3, in which case it returns 7 instead of 8
  It is a latent error until activated
An activated fault becomes effective error
  We call our add and it returns 7 for 5+3
Failure when error results in deviation in behavior
  E.g. we schedule a meeting for the 7th instead of 8th
  An effective error need not result in a failure (if we never use the result of this add, no failure)
Notes: Latent error: hidden error

## Slide 18: Faults Classified by Cause
Hardware Faults
  Hardware devices fail to perform as designed
Design Faults
  Faults in software and some faults in HW
  E.g. the Pentium FDIV bug was a design fault
Operation Faults
  Operator and user mistakes
Environmental Faults
  Fire, power failure, sabotage, etc.
Notes: Pentium FDIV bug is one of the most infamous bugs by Intel. It is a bug in Intel Pentium FPU; for some calculation, it can not produce correct result beyond 4 digits.

## Slide 19: Faults Classified by Duration
Transient Faults
  Last for a limited time and are not recurring
  An alpha particle can flip a bit in memory but usually does not damage the memory HW
Intermittent Faults
  Last for a limited time but are recurring
  E.g. overclocked system works fine for a while, but then crashes… then we reboot it and it does it again
Permanent Faults
  Do not get corrected when time passes
  E.g. the processor has a large round hole in it because we wanted to see what’s inside…
Notes: Alpha particle is a radiation particle that may change the status of memory bits.

## Slide 20: Improving Reliability
Fault Avoidance:
  Prevent occurrence of faults by better HW construction
Fault Tolerance
  Prevent faults from becoming failures
  Typically done through redundancy
Error Removal
  Removing latent errors by verification
Error Forecasting
  Estimate presence, creation, and consequences of errors

## Slide 21: References
Appendix D: Storage Systems
  Online link: http://booksite.elsevier.com/9780123838728/references/appendix_d.pdf