## Slide 1: Pop quiz
What mechanism is used to store the mapping between virtual and physical address spaces?
What mechanism is used to store the mapping between physical address and disk sector spaces?
What mechanism is to transfer data from disk to memory without going through CPU?
Name one condition that triggers page-fault.

## Slide 2: IO Performance

## Slide 3: IO performance
Performance model 1: black-box
  Little’s law:
    Mean number of tasks in system = Arrival rate × Mean response time
Performance model 2
  Queue in front of server
    Queue serves as a buffer before server
  Queuing theory

## Slide 4: IO performance
Metrics
  Throughput, or bandwidth in context of IO
    Maximal arrive rate it can sustain.
  Response time, or latency in context of IO
Trade-off btwn throughput and response time
  Improving throughput favors non-empty queue
  Improving latency favors empty queue

## Slide 5: Throughput versus response time

## Slide 6: SPEC File Server Benchmarks
x
With 168 15k RPM 72GB disks

## Slide 7: CIS 655/CSE 661 - Advanced Computer Architecture
Dr. Yuzhe (Richard) Tang
Interconnect (5.3)

## Slide 8: Networks

## Slide 9: Example 1: On-chip network (ONC)
Many-core: Single-chip cloud computer (SCC)
  48 cores with 2D mesh network
  24 two-core tiles, 4 memory controllers
  Can address totally 64 GB
Has to use 2D mesh to fit into 2D chip

## Slide 10: Example 2: Storage area network
IBM Blue gene: super-computer
  (was) number one in the top500 HPC list
    2,500 square feet
    65,536 dual-processor nodes and 1,024 I/O nodes
  3D torus network: 32*32*64 (=64K)
Chip (node)
2 processors
Compute Card
2 chips
Node Card
16 compute, 0-2 I/O cards
System
64 Racks
Rack
32 Node cards
© Timothy Mark Pinkston, José Duato

## Slide 11: Network Classifications
On-chip Networks (OCNs)
  Sometimes called network-on-chip (NoC)
System/Storage-area Networks (SANs)
  For multi-processor/multi-computer systems, and server-I/O connections
Local Area Networks (LANs)
  100’s-1000’s of nodes; typically up to a few km of distance; usually Ethernet up to 10Gbps
Wide Area Networks (WANs)
  Also called long-haul networks; global-scale; e.g., ATM (asynchronous transfer mode)
nodes

## Slide 12: Example 2: System/storage area net.
InfiniBand
  Industry-wide defacto networking standard
  Can be used for both inter-processor communication or server I/O
  Switch-based technology
  Flexible in topology, arbitration and routing.
    Programmable routing table
  User level communication:
    Send/receive
    RDMA: remotely DMA (redirect memory access) data into the receiver’s memory

## Slide 13: Network interface

## Slide 14: Network Interface Functions
Network functions
  Composing messages
  Packetization
  TCP offload, OS bypassing
  Flow control
  Data transportation
Interconnection Network
End Node
End Node
End Node
End Node
…
Link
Link
Link
Link
…
HW Interface
HW Interface
HW Interface
HW Interface
SW Interface
SW Interface
SW Interface
SW Interface
Device
Device
Device
Device
…
Notes:   Network media
    Electronics: copper
    Optics: e.g. long-distance communication

## Slide 15: Interconnecting Two Devices
proc/mem bus
IO bus or proc/mem bus
Two devices via dedicated link
Communication Protocol
  Typical steps followed by the sender:
    System call by application
      Copies the data into OS and/or network interface memory
      Packetizes the message, Prepares headers and trailers of packets
    Checksum is computed and added to header/trailer
    Timer is started and the network interface sends the packets
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
user
space
system
space
processor
register
file
packet
user writes
data in
memory
system call
sends
1 copy
pipelined
transfer
e.g., DMA
IO bus or proc/mem bus
proc/mem bus
© Timothy Mark Pinkston, José Duato

## Slide 16: Network Interface Functions
Interface Functions
  Composing & processing messages:
    e.g. adding headers
  Packetization
header
Dest
Information
message payload
checksum
trailer
Type
for IP
header
Dest
Info
Msg
ID
Seq.
#
packet payload
checksum
trailer
Type
00 = request
01 = reply
10 = request acknowledge
11 = reply acknowledge

## Slide 17: Interconnecting Two Devices
Communication Protocol
  Typical steps followed by the receiver:
    NI allocates received packets into its memory or OS memory
    Checksum is computed and compared for each packet
      If checksum matches, NI sends back an ACK packet
    Once all packets are correctly received
      The message is reassembled and copied to user's address space
      The corresponding application is signalled (via polling or interrupt)
proc/mem bus
IO bus or proc/mem bus
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
user
space
system
space
processor
register
file
packet
data
ready
interrupt
2 copy
pipelined
reception
e.g., DMA
IO bus or proc/mem bus
proc/mem bus
© Timothy Mark Pinkston, José Duato

## Slide 18: Interconnecting Two Devices
Communication Protocol
  Additional steps at the sender side:
    ACK received: the copy is released and timer is cancelled
    Timer expires before receiving an ACK: packet is resent and the timer is started
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
user
space
system
space
processor
register
file
pkt
ACK
© Timothy Mark Pinkston, José Duato

## Slide 19: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation for DMA transfer to/from memory/NI buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided, protection by OS
proc/mem bus
IO bus or proc/mem bus
processor
memory
user
space
system
space
register
file
ni
FIFO
Interconnection
network
ni
FIFO
memory
system
space
processor
register
file
packet
interrupt:
data ready
Pipelined
peception
e.g., DMA
IO bus or proc/mem bus
proc/mem bus
user copies
data into pinned
user space
system call send.
pipelined transfer
e.g., DMA
user
space
© Timothy Mark Pinkston, José Duato

## Slide 20: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation for DMA transfer to/from memory/NI buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided, protection by OS
  Is it possible to take out register to memory/buffer copy?
proc/mem bus
processor
register
file
ni
FIFO
Interconnection
network
ni
FIFO
packet
processor
register
file
proc/mem bus
memory
system
space
IO bus or proc/mem bus
user
space
IO bus or proc/mem bus
memory
user
space
system
space
© Timothy Mark Pinkston, José Duato

## Slide 21: Interconnecting Two Devices
Communication Protocol
  OS-bypassing (zero-copy or user-level protocols)
    Direct allocation of system or network interface memory/buffers
    Application directly reads/writes from/to these locations
    Memory-to-memory copies are avoided, protection by OS
  Is it possible to take out register to memory/buffer copy?
    NI buffer is associated with (or replaced by) register mapping
proc/mem bus
processor
register
file
ni
FIFO
Interconnection
network
ni
FIFO
packet
processor
register
file
proc/mem bus
Pipelined transfer
© Timothy Mark Pinkston, José Duato

## Slide 22: Extra Network Interface Functions
Network functions
  TCP offload from host CPU to NIC processors
    Works for SAN, LAN and WAN.
  Flow control:
    Prevent sending packets faster than can be processed by receivers
    Strategy: receiver notifies sender to stop now & resume later
  Transport over physical layer
    Express the packets in signal and physically transport signal
Memory
NIC
DMA
DMA
NIC
processor
internal interconnect
FIFO
Network
interface
to/from
network
host interface

## Slide 23: Blackbox view of the network
Black-box model of interconnection network
  Deliver packets from one node to another
    About packets not messages
    Not about network stack: App-level protocols
proc/mem bus
processor
register
file
ni
FIFO
Interconnection
network
ni
FIFO
packet
processor
register
file
proc/mem bus
Pipelined transfer
What happens internally?

## Slide 24: Internal Network Design
More than 2 devices:
  Paths need to be shared  how?
Topology: network structure
  “What paths are possible for a packet?”
  Shared- or switched-media
Routing:
  ”Which of the possible paths are valid for packets?”
  Outcome: Determine a path from source to destination
    Routing info in packet header
Arbitration:
  “When are paths available for packets?”
  Outcome: One winner to advance to the next step (by switching), several losers to buffer
    Flow control: avoids buffer overflow
Switching:
  “How are paths allocated to packets?”

## Slide 25: Network Structure

## Slide 26: Interconnection networks: Shared media
Traditionally just used a bus (or shared media)

## Slide 27: Shared Media Networks
Need arbitration to decide who gets to talk
Arbitration can be centralized or distributed
Distributed arbitration
  (Centralized not used much in practice)
  Check, if media not used now, start sending
  if another also sending (collision detection)
  If collision, wait for a while and retry
    “For a while” is random (otherwise collisions repeat forever)
    Exponential back-off to avoid wasting bandwidth on collisions
  Not scalable

## Slide 28: Interconnection Networks: Switched
Large-scale systems:
  Massive MP systems (many-core), for instance:
    Intel’s Single-chip Cloud computer
    HPC (top500 computers)
  The Internet
Switched networks
Notes: ATM: Asynchronous Transfer Mode

## Slide 29: Switched Networks
Switching: allocating path to packets
  From the input port/buffer to the output
  Switching overheads but no time wasted on arbitration
    Multiple transfers can be in progress
      If they use different links, of course
Circuit or Packet Switching
  Circuit-level switching: per end-to-end connection
    Reserves links for a connection (e.g., phone network)
  Packet-level switching: each packet routed separately
    Links used only when data transferred (e.g., Internet Protocol)

## Slide 30: Switch Technology
What do we want in a switch
  Many input and output links
    Usually number of input and output links the same
  Low contention inside the switch
    Best if there is none (only external links cause contention)
  Short switching delay

## Slide 31: Crossbar Switch
Crossbar
  Very low switching delay, no internal contention
  Complexity grows as square of number of links
    Can not have too many links (e.g., up to 64 in and 64 out)

## Slide 32: Omega Network
Omega Network
  Build switches with more ports using small crossbars
  Lower complexity per link, but longer delay and more contention

## Slide 33: Connecting switches: Network Topology
Mesh
Torus

## Slide 34: Connecting Switches: Network Topology
Hypercube

## Slide 35: Network Topology: Metrics
What do we want in a network topology
  Many nodes, high bandwidth, low contention, low latency
  Low latency: few switches along any route
    For each (src, dest) pair, we choose shortest route
    Longest such route over all (src,dst) pairs: network diameter
    We want networks with small diameter!
  Low contention: high aggregate bandwidth
    Divide network into two groups, each with half the nodes
    Total bandwidth between groups is bisection bandwidth
    Actually, we use the minimum over all such bisections
  Low switch complexity: higher switch speeds
    Want low in-/out-degree for node

## Slide 36: Example Topologies (Chain)
Diameter
Average Distance
Bisection Bandwidth
Max degree
Notes: Diameter: 4
Average distance: 2 =(1*4+2*3+3*2+4*1) / (1+2+3+4)
Bisection bandwidth: 1
Max degree: 2

## Slide 37: Example Topologies (Ring)
Diameter
Average Distance
Bisection Bandwidth
Max degree
Notes: Diameter: 2
Average distance: 1.5=(1+2+2+1) / 4 (symmetry)
Bisection bandwidth: 2
Max degree: 2

## Slide 38: Example Topologies (2D Grid/Mesh)
Diameter
Average Distance
Bisection Bandwidth
Max degree
Notes: Diameter: 4
Average distance: 2
Bisection bandwidth: 4
Max degree: 4

## Slide 39: Different Topologies, Different Uses
Chain networks
2D mesh networks: on-chip interconnects
Hyper-cube networks: SAN

## Slide 40: Example Topologies (2D Torus)
Diameter
Average Distance
Bisection Bandwidth
Max degree

## Slide 41: Example Topologies (Hyper-Cube)
Diameter
Average Distance
Bisection Bandwidth
Max degree

## Slide 42: Routing

## Slide 43: Routing
Shared media has trivial routing (broadcast)
In switched media we can have
  Source-based (source specifies route)
  Virtual circuits (end-to-end route created)
    When connection made, set up route
    Switches forward packets along the route
  Destination-based (source specifies destination)
    Switches must route packet toward destination
Also can be classified into
  Deterministic (one unique route from a source to a destination)
  Adaptive (different routes can be used)

## Slide 44: Routing Methods for Switches
Store-and-Forward
  Switch receives entire packet, then forwards it
  If error occurs when forwarding, switch can re-send
Timeline
H
B
B
B
T
H
B
B
B
T
H
B
B
B
T
Channel
0
1
2
3

## Slide 45: Wormhole routing
Packet consists of flits (a few bytes each)
  Each flit is the amount of data can be transferred in one clock cycle
First flit contains header w/ destination address
Switch gets header, decides where to forward
Other flits (without header) forwarded as they arrive
    Between flits, it does not allow other package to cut in.
Looks like packet worming through network
If an error occurs along the way, sender must resend
  No switch has the entire packet to re-send it
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14
Cycle
Channel
H
B
B
B
T
H
B
B
B
T
H
B
B
B
T
0
1
2
3

## Slide 46: Flow control in wormhole routing
Each network link starts/terminates in a buffer in the switch port.
Flow control: resource allocations in the buffer
Wormhole routing: per-flit allocation
  Allocate one flit-sized buffer upon arrival of one flit
What if the link is busy (dest. buffer being full) in the middle of a transfer?
  How to deal with the rest of flits in the packet?
Wormhole has to stop the tail when head stops
  Now each flit along the way blocks a link
  One busy link creates other busy links => traffic jam

## Slide 47: Cut-Through Routing
Cut-through routing:
  Allocate dest. buffer per packet
  Before the header is transferred, make sure there is enough space for the packet.
Handling busy links
  If outgoing link busy, receive and buffer incoming flits
  The buffered flits stay there until link becomes free
  When link free, the flits start worming out of the switch
  Need packet-sized buffer space in each switch
    Wormhole Routing switch needs to buffer only one flit

## Slide 48: Routing: Network Latency
Switch Delay
  Time from incoming to outgoing link in a switch
Switches
  Number of switches along the way
Transfer time
  Time to send the packet through a link
Store-and-Forward end-to-end transfer time
  (Switches*SwitchDelay)+(TransferTime*(Switches+1))
Wormhole end-to-end transfer time
  (Switches*SwitchDelay) + TransferTime
  Much better if there are many switches along the way

## Slide 49: S&F vs. Wormhole
Assume network with 7 switches on route to send a message. 16 bytes messages, 4 byte headers, 0.25 ms switch latency, transfer rate of 20MB/s
  Packet size:
  Time to transfer over one link:
  S&F Time: (#Sw * Sw-delay) + ((#Sw +1) + transfer_time)
  Wormhole Time: (#Sw * Sw-delay) + transfer_time

## Slide 50: References
Appendix F:
  Online link: http://booksite.elsevier.com/9780123838728/references/appendix_f.pdf
Copyright © 2012, Elsevier Inc. All rights reserved.